## Slide 1: FPGAs and Programming in Cascade
eric schkufza
November 7, 2018

## Slide 2
FPGAs
  What’s so good about them? What’s so bad about them?
Cascade
  How we make the good stuff better, and the bad stuff less awful
Live Demo
  Writing a simple program in Cascade
Time Permitting
  How Cascade works? Verilog minutiae?

## Slide 3: What are FPGAs good for?
FPGAs make sense when:
  A workload is high-performance but also predictable
  Application requirements change relatively frequently
Performance
Generality
FPGA
CPU
ASIC

## Slide 4: But programming an FPGA is HARD!
Verilog is complicated:
  Mix of concurrent and sequential semantics
  Awkward type system
  Half-baked meta-programming
  Synthesizable vs unsynthesizable code
Domain-specific Languages
  Chisel, Halide, etc…
Bad Design
Good Design
Widely Used
Niche
Haskell
C/C++
Java
JavaScript
R
Verilog

## Slide 5: And compilation takes FOREVER!
Software Compilers:
  O(seconds)
  Reason about programs locally
  Pre-defined O(n^k) rules
Software Development:
  Compile-test-debug cycle
  Test and deploy in the same environment
Hardware Compilers:
  O(minutes to hours)
  Reason about programs globally
  NP-hard constraint satisfaction
Hardware Development:
  Debug behavior in a simulator
  Debug timing in hardware
  Test and deploy in different environments

## Slide 6
CASCADE
Makes programming hardware feel like programming software
Notes: Run code in seconds
Printf from hardware
Preserves performance to within 3x of native compilation

## Slide 7: Design Goals
Interactivity
  Modify a running program, I/O side effects visible immediately
Expressiveness
  Eliminate synthesizable vs non-synthesizable distinction
Portability
  Write code once, run on many platforms with little modification
Performance
  Don’t pay for features you don’t use

## Slide 8: Interactivity
Just-in-Time Compilation
  Code runs immediately in a simulator
  Compilation takes place in the background
  Control switches when compilation is done
  Code appears to run faster over time
Why can we do this?
  What’s the meaning of a Verilog program?
  What’s the meaning of any program?

## Slide 9: Interactivity
Just-in-Time Compilation
  Code runs immediately in a simulator
  Compilation takes place in the background
  Control switches when compilation is done
  Code appears to run faster over time
Why can we do this?
  What’s the meaning of a Verilog program?

## Slide 10: Expressiveness
Unsynthesizable Verilog in hardware
  Display statements
  Finish statements
  Longer term: support for the entire unsynthesizable language subset
Why can we do this?
  What is Cascade doing differently compared to a traditional compiler?

## Slide 11: Expressiveness

## Slide 12: Limitations and Future Work
Non-Monotonic language features
  Code deletion
  Genvar statements
Timing-sensitive applications
  A giga-bit ethernet switch?
  A peripheral which expects inputs on a perfectly periodic clock?
FPGA Virtualization:
  Share one FPGA between two instances of Cascade
  Use Cascade to transparently run one very large program on two separate FPGAs
Speculative Optimization:
  Specialize the implementation of a program to the values that it sees at runtime
  Generate smaller / faster code

## Slide 13: Thank You
Questions on Piazza
Bug Reports on https://github.com/vmware/cascade