## Slide 1: Machine-Level Programming I: Basics CS 429H: Systems I
Instructor:
Emmett Witchel

## Slide 2: Today: Machine Programming I: Basics
History of Intel processors and architectures
C, assembly, machine code
Assembly Basics: Registers, operands, move

## Slide 3: Intel x86 Processors
Totally dominate laptop/desktop/server market
Evolutionary design
  Backwards compatible up until 8086, introduced in 1978
  Added more features as time goes on
Complex instruction set computer (CISC)
  Many different instructions with many different formats
    But, only small subset encountered with Linux programs
  Hard to match performance of Reduced Instruction Set Computers (RISC)
  But, Intel has done just that!
    In terms of speed. Less so for low power.

## Slide 4: Intel x86 Evolution: Milestones
Name Date Transistors MHz
8086 1978 29K 5-10
  First 16-bit processor. Basis for IBM PC & DOS
  1MB address space
386 1985 275K 16-33
  First 32 bit processor , referred to as IA32
  Added “flat addressing”
  Capable of running Unix
  32-bit Linux/gcc uses no instructions introduced in later models
Pentium 4F 2004 125M 2800-3800
  First 64-bit processor, referred to as x86-64
Core i7 2008 731M 2667-3333

## Slide 5: Intel x86 Processors: Overview
X86-64 / EM64t
X86-32/IA32
X86-16
8086
286
386
486
Pentium
Pentium MMX
Pentium III
Pentium 4
Pentium 4E
Pentium 4F
Core 2 Duo
Core i7
IA: often redefined as latest Intel architecture
time
Architectures
Processors
MMX
SSE
SSE2
SSE3
SSE4

## Slide 6: Intel x86 Processors, contd.
Machine Evolution
  386 1985 0.3M
  Pentium 1993 3.1M
  Pentium/MMX 1997 4.5M
  PentiumPro 1995 6.5M
  Pentium III 1999 8.2M
  Pentium 4 2001 42M
  Core 2 Duo 2006 291M
  Core i7 2008 731M
Added Features
  Instructions to support multimedia operations
    Parallel operations on 1, 2, and 4-byte data, both integer & FP
  Instructions to enable more efficient conditional operations
Linux/GCC Evolution
  Two major steps: 1) support 32-bit 386. 2) support 64-bit x86-64

## Slide 7: More Information
Intel processors (Wikipedia)
Intel microarchitectures

## Slide 8: New Species: ia64, then IPF, then Itanium
Name Date Transistors
Itanium 2001 10M
  First shot at 64-bit architecture: first called IA64
  Radically new instruction set designed for high performance
  Can run existing IA32 programs
    On-board “x86 engine”
  Joint project with Hewlett-Packard
Itanium 2 2002 221M
  Big performance boost
Itanium 2 Dual-Core 2006 1.7B
Itanium has not taken off in marketplace
  Lack of backward compatibility, no good compiler support, Pentium 4 got too good

## Slide 9: x86 Clones: Advanced Micro Devices (AMD)
Historically
  AMD has followed just behind Intel
  A little bit slower, a lot cheaper
Then
  Recruited top circuit designers from Digital Equipment Corp. and other downward trending companies
  Built Opteron: tough competitor to Pentium 4
  Developed x86-64, their own extension to 64 bits

## Slide 10: Intel’s 64-Bit
Intel Attempted Radical Shift from IA32 to IA64
  Totally different architecture (Itanium)
  Executes IA32 code only as legacy
  Performance disappointing
AMD Stepped in with Evolutionary Solution
  x86-64 (now called “AMD64”)
Intel Felt Obligated to Focus on IA64
  Hard to admit mistake or that AMD is better
2004: Intel Announces EM64T extension to IA32
  Extended Memory 64-bit Technology
  Almost identical to x86-64!
All but low-end x86 processors support x86-64
  But, lots of code still runs in 32-bit mode

## Slide 11: Our Coverage
IA32
  The traditional x86
x86-64/EM64T
  The emerging standard
Presentation
  Book presents IA32 in Sections 3.1—3.12
  Covers x86-64 in 3.13

## Slide 12: Today: Machine Programming I: Basics
History of Intel processors and architectures
C, assembly, machine code
Assembly Basics: Registers, operands, move

## Slide 13: Definitions
Architecture: (also instruction set architecture: ISA) The parts of a processor design that one needs to understand to write assembly code.
  Examples: instruction set specification, registers.
Microarchitecture: Implementation of the architecture.
  Examples: cache sizes and core frequency.
Example ISAs (Intel): x86, IA, IPF

## Slide 14: Assembly Programmer’s View
CPU
Programmer-Visible State
  PC: Program counter
    Address of next instruction
    Called “EIP” (IA32) or “RIP” (x86-64)
  Register file
    Heavily used program data
  Condition codes
    Store status information about most recent arithmetic operation
    Used for conditional branching
  Memory
    Byte addressable array
    Code, user data, (some) OS data
    Includes stack used to support procedures
PC
Registers
Memory
Object Code
Program Data
OS Data
Addresses
Data
Instructions
Stack
Condition
Codes

## Slide 15: Program to Process
We write a program in e.g., C.
A compiler turns that program into an instruction list.
The CPU interprets the instruction list (which is more a graph of basic blocks).
  void X (int b) {
  if(b == 1) {
  …
  int main() {
  int a = 2;
  X(a);
  }

## Slide 16: Process in Memory
Program to process.
  void X (int b) {
  if(b == 1) {
  …
  int main() {
  int a = 2;
  X(a);
  }
What you wrote
What is in memory.
  void X (int b) {
  if(b == 1) {
  …
  int main() {
  int a = 2;
  X(a);
  }
Code
main; a = 2
X; b = 2
Heap
Stack
What must the OS track for a process?

## Slide 17: A shell forks and execs a calculator
pid = 127
open files = “.history”
last_cpu = 0
pid = 128
open files = “.history”
last_cpu = 0
int pid = fork();
if(pid == 0) {
close(“.history”);
exec(“/bin/calc”);
} else {
wait(pid);
int pid = fork();
if(pid == 0) {
close(“.history”);
exec(“/bin/calc”);
} else {
wait(pid);
Process Control
Blocks (PCBs)
OS
USER
int pid = fork();
if(pid == 0) {
close(“.history”);
exec(“/bin/calc”);
} else {
wait(pid);
int calc_main(){
int q = 7;
do_init();
ln = get_input();
exec_in(ln);
pid = 128
open files =
last_cpu = 0
int pid = fork();
if(pid == 0) {
close(“.history”);
exec(“/bin/calc”);
} else {
wait(pid);

## Slide 18: A shell forks and then execs a calculator
pid = 127
open files = “.history”
last_cpu = 0
pid = 128
open files = “.history”
last_cpu = 0
int shell_main() {
int a = 2;
…
Code
main; a = 2
Heap
Stack
0xFC0933CA
int shell_main() {
int a = 2;
…
Code
main; a = 2
Heap
Stack
0xFC0933CA
int calc_main() {
int q = 7;
…
Code
Heap
Stack
0x43178050
pid = 128
open files =
last_cpu = 0
Process Control
Blocks (PCBs)
OS
USER

## Slide 19: Anatomy of an address space
Code
Header
Initialized data
Executable File
Code
Initialized data
Heap
Stack
DLL’s
mapped segments
Process’s
address space
Inaccessible

## Slide 20: Turning C into Object Code
text
text
binary
binary
Compiler (gcc -S)
Assembler (gcc or as)
Linker (gcc or ld)
C program (p1.c p2.c)
Asm program (p1.s p2.s)
Object program (p1.o p2.o)
Executable program (p)
Static libraries (.a)
  Code in files p1.c p2.c
  Compile with command: gcc –O1 p1.c p2.c -o p
    Use basic optimizations (-O1)
    Put resulting binary in file p

## Slide 21: Compiling Into Assembly
C Code
int sum(int x, int y)
{
int t = x+y;
return t;
}
Generated IA32 Assembly
sum:
pushl %ebp
movl %esp,%ebp
movl 12(%ebp),%eax
addl 8(%ebp),%eax
popl %ebp
ret
Obtain with command
  /usr/local/bin/gcc –O1 -S code.c
Produces file code.s
Some compilers use instruction “leave”

## Slide 22: Assembly Characteristics: Data Types
“Integer” data of 1, 2, or 4 bytes
  Data values
  Addresses (untyped pointers)
Floating point data of 4, 8, or 10 bytes
No aggregate types such as arrays or structures
  Just contiguously allocated bytes in memory

## Slide 23: Assembly Characteristics: Operations
Perform arithmetic function on register or memory data
Transfer data between memory and register
  Load data from memory into register
  Store register data into memory
Transfer control
  Unconditional jumps to/from procedures
  Conditional branches

## Slide 24: Object Code
Code for sum
0x401040 <sum>:
0x55
0x89
0xe5
0x8b
0x45
0x0c
0x03
0x45
0x08
0x5d
0xc3
Assembler
  Translates .s into .o
  Binary encoding of each instruction
  Nearly-complete image of executable code
  Missing linkages between code in different files
Linker
  Resolves references between files
  Combines with static run-time libraries
    E.g., code for malloc, printf
  Some libraries are dynamically linked
    Linking occurs when program begins execution
  Total of 11 bytes
  Each instruction 1, 2, or 3 bytes
  Starts at address 0x401040

## Slide 25: Machine Instruction Example
C Code
  Add two signed integers
Assembly
  Add 2 4-byte integers
    “Long” words in GCC parlance
    Same instruction whether signed or unsigned
  Operands:
    x: Register %eax
    y: Memory M[%ebp+8]
    t: Register %eax
      Return function value in %eax
Object Code
  3-byte instruction
  Stored at address 0x80483ca
int t = x+y;
addl 8(%ebp),%eax
0x80483ca: 03 45 08
Similar to expression:
x += y
More precisely:
int eax;
int *ebp;
eax += ebp[2]

## Slide 26: Disassembling Object Code
Disassembled
Disassembler
  objdump -d p
  Useful tool for examining object code
  Analyzes bit pattern of series of instructions
  Produces approximate rendition of assembly code
  Can be run on either a.out (complete executable) or .o file
080483c4 <sum>:
80483c4: 55 push %ebp
80483c5: 89 e5 mov %esp,%ebp
80483c7: 8b 45 0c mov 0xc(%ebp),%eax
80483ca: 03 45 08 add 0x8(%ebp),%eax
80483cd: 5d pop %ebp
80483ce: c3 ret

## Slide 27: Alternate Disassembly
Disassembled
Dump of assembler code for function sum:
0x080483c4 <sum+0>: push %ebp
0x080483c5 <sum+1>: mov %esp,%ebp
0x080483c7 <sum+3>: mov 0xc(%ebp),%eax
0x080483ca <sum+6>: add 0x8(%ebp),%eax
0x080483cd <sum+9>: pop %ebp
0x080483ce <sum+10>: ret
Within gdb Debugger
  gdb p
  disassemble sum
  Disassemble procedure
  x/11xb sum
  Examine the 11 bytes starting at sum
Object
0x401040:
0x55
0x89
0xe5
0x8b
0x45
0x0c
0x03
0x45
0x08
0x5d
0xc3

## Slide 28: What Can be Disassembled?
Anything that can be interpreted as executable code
Disassembler examines bytes and reconstructs assembly source
% objdump -d WINWORD.EXE
WINWORD.EXE: file format pei-i386
No symbols in "WINWORD.EXE".
Disassembly of section .text:
30001000 <.text>:
30001000: 55 push %ebp
30001001: 8b ec mov %esp,%ebp
30001003: 6a ff push $0xffffffff
30001005: 68 90 10 00 30 push $0x30001090
3000100a: 68 91 dc 4c 30 push $0x304cdc91

## Slide 29: Today: Machine Programming I: Basics
History of Intel processors and architectures
C, assembly, machine code
Assembly Basics: Registers, operands, move

## Slide 30: Integer Registers (IA32)
%eax
%ecx
%edx
%ebx
%esi
%edi
%esp
%ebp
%ax
%cx
%dx
%bx
%si
%di
%sp
%bp
%ah
%ch
%dh
%bh
%al
%cl
%dl
%bl
16-bit virtual registers
(backwards compatibility)
general purpose
accumulate
counter
data
base
source
index
destination
index
stack
pointer
base
pointer
Origin
(mostly obsolete)

## Slide 31: Moving Data: IA32
Moving Data
  movl Source, Dest:
Operand Types
  Immediate: Constant integer data
    Example: $0x400, $-533
    Like C constant, but prefixed with ‘$’
    Encoded with 1, 2, or 4 bytes
  Register: One of 8 integer registers
    Example: %eax, %edx
    But %esp and %ebp reserved for special use
    Others have special uses for particular instructions
  Memory: 4 consecutive bytes of memory at address given by register
    Simplest example: (%eax)
    Various other “address modes”
%eax
%ecx
%edx
%ebx
%esi
%edi
%esp
%ebp

## Slide 32: movl Operand Combinations
Cannot do memory-memory transfer with a single instruction
movl
Imm
Reg
Mem
Reg
Mem
Reg
Mem
Reg
Source
Dest
C Analog
movl $0x4,%eax
temp = 0x4;
movl $-147,(%eax)
*p = -147;
movl %eax,%edx
temp2 = temp1;
movl %eax,(%edx)
*p = temp;
movl (%eax),%edx
temp = *p;
Src,Dest

## Slide 33: Simple Memory Addressing Modes
Normal (R) Mem[Reg[R]]
  Register R specifies memory address movl (%ecx),%eax
Displacement D(R) Mem[Reg[R]+D]
  Register R specifies start of memory region
  Constant displacement D specifies offset movl 8(%ebp),%edx

## Slide 34: Using Simple Addressing Modes
void swap(int *xp, int *yp)
{
int t0 = *xp;
int t1 = *yp;
*xp = t1;
*yp = t0;
}
Body
Set
Up
Finish
swap:
pushl %ebp
movl %esp,%ebp
pushl %ebx
movl 8(%ebp), %edx
movl 12(%ebp), %ecx
movl (%edx), %ebx
movl (%ecx), %eax
movl %eax, (%edx)
movl %ebx, (%ecx)
popl %ebx
popl %ebp
ret

## Slide 35: Using Simple Addressing Modes
void swap(int *xp, int *yp)
{
int t0 = *xp;
int t1 = *yp;
*xp = t1;
*yp = t0;
}
swap:
pushl %ebp
movl %esp,%ebp
pushl %ebx
movl 8(%ebp), %edx
movl 12(%ebp), %ecx
movl (%edx), %ebx
movl (%ecx), %eax
movl %eax, (%edx)
movl %ebx, (%ecx)
popl %ebx
popl %ebp
ret
Body
Set
Up
Finish

## Slide 36: Understanding Swap
void swap(int *xp, int *yp)
{
int t0 = *xp;
int t1 = *yp;
*xp = t1;
*yp = t0;
}
Stack
(in memory)
Register Value
%edx xp
%ecx yp
%ebx t0
%eax t1
yp
xp
Rtn adr
Old %ebp
%ebp
0
4
8
12
Offset
•
•
•
Old %ebx
-4
%esp
movl 8(%ebp), %edx # edx = xp
movl 12(%ebp), %ecx # ecx = yp
movl (%edx), %ebx # ebx = *xp (t0)
movl (%ecx), %eax # eax = *yp (t1)
movl %eax, (%edx) # *xp = t1
movl %ebx, (%ecx) # *yp = t0

## Slide 37: Understanding Swap
0x120
0x124
Rtn adr
%ebp
0
4
8
12
Offset
-4
123
456
Address
0x124
0x120
0x11c
0x118
0x114
0x110
0x10c
0x108
0x104
0x100
yp
xp
%eax
%edx
%ecx
%ebx
%esi
%edi
%esp
%ebp
0x104
movl 8(%ebp), %edx # edx = xp
movl 12(%ebp), %ecx # ecx = yp
movl (%edx), %ebx # ebx = *xp (t0)
movl (%ecx), %eax # eax = *yp (t1)
movl %eax, (%edx) # *xp = t1
movl %ebx, (%ecx) # *yp = t0

## Slide 38: Understanding Swap
0x120
0x124
Rtn adr
%ebp
0
4
8
12
Offset
-4
123
456
Address
0x124
0x120
0x11c
0x118
0x114
0x110
0x10c
0x108
0x104
0x100
yp
xp
%eax
%edx
%ecx
%ebx
%esi
%edi
%esp
%ebp
0x124
0x104
0x120
movl 8(%ebp), %edx # edx = xp
movl 12(%ebp), %ecx # ecx = yp
movl (%edx), %ebx # ebx = *xp (t0)
movl (%ecx), %eax # eax = *yp (t1)
movl %eax, (%edx) # *xp = t1
movl %ebx, (%ecx) # *yp = t0

## Slide 39: Understanding Swap
0x120
0x124
Rtn adr
%ebp
0
4
8
12
Offset
-4
123
456
Address
0x124
0x120
0x11c
0x118
0x114
0x110
0x10c
0x108
0x104
0x100
yp
xp
%eax
%edx
%ecx
%ebx
%esi
%edi
%esp
%ebp
0x120
0x104
0x124
0x124
movl 8(%ebp), %edx # edx = xp
movl 12(%ebp), %ecx # ecx = yp
movl (%edx), %ebx # ebx = *xp (t0)
movl (%ecx), %eax # eax = *yp (t1)
movl %eax, (%edx) # *xp = t1
movl %ebx, (%ecx) # *yp = t0

## Slide 40: Understanding Swap
456
0x120
0x124
Rtn adr
%ebp
0
4
8
12
Offset
-4
123
456
Address
0x124
0x120
0x11c
0x118
0x114
0x110
0x10c
0x108
0x104
0x100
yp
xp
%eax
%edx
%ecx
%ebx
%esi
%edi
%esp
%ebp
0x124
0x120
123
0x104
movl 8(%ebp), %edx # edx = xp
movl 12(%ebp), %ecx # ecx = yp
movl (%edx), %ebx # ebx = *xp (t0)
movl (%ecx), %eax # eax = *yp (t1)
movl %eax, (%edx) # *xp = t1
movl %ebx, (%ecx) # *yp = t0

## Slide 41: Understanding Swap
0x120
0x124
Rtn adr
%ebp
0
4
8
12
Offset
-4
123
456
Address
0x124
0x120
0x11c
0x118
0x114
0x110
0x10c
0x108
0x104
0x100
yp
xp
%eax
%edx
%ecx
%ebx
%esi
%edi
%esp
%ebp
456
0x124
0x120
0x104
123
123
movl 8(%ebp), %edx # edx = xp
movl 12(%ebp), %ecx # ecx = yp
movl (%edx), %ebx # ebx = *xp (t0)
movl (%ecx), %eax # eax = *yp (t1)
movl %eax, (%edx) # *xp = t1
movl %ebx, (%ecx) # *yp = t0

## Slide 42: Understanding Swap
456
456
0x120
0x124
Rtn adr
%ebp
0
4
8
12
Offset
-4
Address
0x124
0x120
0x11c
0x118
0x114
0x110
0x10c
0x108
0x104
0x100
yp
xp
%eax
%edx
%ecx
%ebx
%esi
%edi
%esp
%ebp
456
456
0x124
0x120
123
0x104
123
movl 8(%ebp), %edx # edx = xp
movl 12(%ebp), %ecx # ecx = yp
movl (%edx), %ebx # ebx = *xp (t0)
movl (%ecx), %eax # eax = *yp (t1)
movl %eax, (%edx) # *xp = t1
movl %ebx, (%ecx) # *yp = t0

## Slide 43: Understanding Swap
0x120
0x124
Rtn adr
%ebp
0
4
8
12
Offset
-4
456
123
Address
0x124
0x120
0x11c
0x118
0x114
0x110
0x10c
0x108
0x104
0x100
yp
xp
%eax
%edx
%ecx
%ebx
%esi
%edi
%esp
%ebp
456
0x124
0x120
0x104
123
123
movl 8(%ebp), %edx # edx = xp
movl 12(%ebp), %ecx # ecx = yp
movl (%edx), %ebx # ebx = *xp (t0)
movl (%ecx), %eax # eax = *yp (t1)
movl %eax, (%edx) # *xp = t1
movl %ebx, (%ecx) # *yp = t0

## Slide 44: Complete Memory Addressing Modes
Most General Form
D(Rb,Ri,S) Mem[Reg[Rb]+S*Reg[Ri]+ D]
  D: Constant “displacement” 1, 2, or 4 bytes
  Rb: Base register: Any of 8 integer registers
  Ri: Index register: Any, except for %esp
    Unlikely you’d use %ebp, either
  S: Scale: 1, 2, 4, or 8 (why these numbers?)
Special Cases
(Rb,Ri) Mem[Reg[Rb]+Reg[Ri]]
D(Rb,Ri) Mem[Reg[Rb]+Reg[Ri]+D]
(Rb,Ri,S) Mem[Reg[Rb]+S*Reg[Ri]]

## Slide 45: Today: Machine Programming I: Basics
History of Intel processors and architectures
C, assembly, machine code
Assembly Basics: Registers, operands, move
Intro to x86-64

## Slide 46: Data Representations: IA32 + x86-64
Sizes of C Objects (in Bytes)
  C Data Type Generic 32-bit Intel IA32 x86-64
    unsigned 4 4 4
    int 4 4 4
    long int 4 4 8
    char 1 1 1
    short 2 2 2
    float 4 4 4
    double 8 8 8
    long double 8 10/12 16
    char * 4 4 8
      Or any other pointer

## Slide 47: x86-64 Integer Registers
%rsp
  Extend existing registers. Add 8 new ones.
  Make %ebp/%rbp general purpose
%eax
%ebx
%ecx
%edx
%esi
%edi
%esp
%ebp
%r8d
%r9d
%r10d
%r11d
%r12d
%r13d
%r14d
%r15d
%r8
%r9
%r10
%r11
%r12
%r13
%r14
%r15
%rax
%rbx
%rcx
%rdx
%rsi
%rdi
%rbp

## Slide 48: Instructions
Long word l (4 Bytes) ↔ Quad word q (8 Bytes)
New instructions:
  movl ➙ movq
  addl ➙ addq
  sall ➙ salq
  etc.
32-bit instructions that generate 32-bit results
  Set higher order bits of destination register to 0
  Example: addl

## Slide 49: 32-bit code for swap
void swap(int *xp, int *yp)
{
int t0 = *xp;
int t1 = *yp;
*xp = t1;
*yp = t0;
}
Body
Set
Up
Finish
swap:
pushl %ebp
movl %esp,%ebp
pushl %ebx
movl 8(%ebp), %edx
movl 12(%ebp), %ecx
movl (%edx), %ebx
movl (%ecx), %eax
movl %eax, (%edx)
movl %ebx, (%ecx)
popl %ebx
popl %ebp
ret

## Slide 50: 64-bit code for swap
Operands passed in registers (why useful?)
  First (xp) in %rdi, second (yp) in %rsi
  64-bit pointers
No stack operations required
32-bit data
  Data held in registers %eax and %edx
  movl operation
void swap(int *xp, int *yp)
{
int t0 = *xp;
int t1 = *yp;
*xp = t1;
*yp = t0;
}
Body
Set
Up
Finish
swap:
movl (%rdi), %edx
movl (%rsi), %eax
movl %eax, (%rdi)
movl %edx, (%rsi)
ret

## Slide 51: 64-bit code for long int swap
64-bit data
  Data held in registers %rax and %rdx
  movq operation
    “q” stands for quad-word
void swap(long *xp, long *yp)
{
long t0 = *xp;
long t1 = *yp;
*xp = t1;
*yp = t0;
}
Body
Set
Up
Finish
swap_l:
movq (%rdi), %rdx
movq (%rsi), %rax
movq %rax, (%rdi)
movq %rdx, (%rsi)
ret

## Slide 52: Machine Programming I: Summary
History of Intel processors and architectures
  Evolutionary design leads to many quirks and artifacts
C, assembly, machine code
  Compiler must transform statements, expressions, procedures into low-level instruction sequences
Assembly Basics: Registers, operands, move
  The x86 move instructions cover wide range of data movement forms
Intro to x86-64
  A major departure from the style of code seen in IA32