## Slide 1: Cache Memories

## Slide 2: Today
Cache memory organization and operation
Performance impact of caches
  The memory mountain
  Rearranging loops to improve spatial locality
  Using blocking to improve temporal locality

## Slide 3: Cache Memories
Cache memories are small, fast SRAM-based memories managed automatically in hardware.
  Hold frequently accessed blocks of main memory
CPU looks first for data in caches (e.g., L1, L2, and L3), then in main memory.
Typical system structure:
Main
memory
I/O
bridge
Bus interface
ALU
Register file
CPU chip
System bus
Memory bus
Cache
memories

## Slide 4: General Cache Organization (S, E, B)
E = 2e lines per set
S = 2s sets
set
line
0
1
2
B-1
tag
v
B = 2b bytes per cache block (the data)
Cache size:
C = S x E x B data bytes
valid bit

## Slide 5: Cache Read
E = 2e lines per set
S = 2s sets
0
1
2
B-1
tag
v
valid bit
B = 2b bytes per cache block (the data)
t bits
s bits
b bits
Address of word:
tag
set
index
block
offset
data begins at this offset
Locate set
Check if any line in set has matching tag
Yes + line valid: hit
Locate data starting at offset

## Slide 6: Example: Direct Mapped Cache (E = 1)
S = 2s sets
Direct mapped: One line per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
find set

## Slide 7: Example: Direct Mapped Cache (E = 1)
Direct mapped: One line per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
match: assume yes = hit
valid? +
block offset
tag

## Slide 8: Example: Direct Mapped Cache (E = 1)
Direct mapped: One line per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
match: assume yes = hit
valid? +
int (4 Bytes) is here
block offset
No match: old line is evicted and replaced

## Slide 9: Direct-Mapped Cache Simulation
M=16 byte addresses, B=2 bytes/block,
S=4 sets, E=1 Blocks/set
Address trace (reads, one byte per read):
0 [00002],
1 [00012],
7 [01112],
8 [10002],
0 [00002]
x
t=1
s=2
b=1
xx
x
0
?
?
v
Tag
Block
miss
1
0
M[0-1]
hit
miss
1
0
M[6-7]
miss
1
1
M[8-9]
miss
1
0
M[0-1]
Set 0
Set 1
Set 2
Set 3

## Slide 10: A Higher Level Example
int sum_array_rows(double a[16][16])
{
int i, j;
double sum = 0;
for (i = 0; i < 16; i++)
for (j = 0; j < 16; j++)
sum += a[i][j];
return sum;
}
32 B = 4 doubles
assume: cold (empty) cache,
a[0][0] goes here
int sum_array_cols(double a[16][16])
{
int i, j;
double sum = 0;
for (j = 0; i < 16; i++)
for (i = 0; j < 16; j++)
sum += a[i][j];
return sum;
}
blackboard
Ignore the variables sum, i, j

## Slide 11: E-way Set Associative Cache (Here: E = 2)
E = 2: Two lines per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of short int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
find set

## Slide 12: E-way Set Associative Cache (Here: E = 2)
E = 2: Two lines per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of short int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
compare both
valid? +
match: yes = hit
block offset
tag

## Slide 13: E-way Set Associative Cache (Here: E = 2)
E = 2: Two lines per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of short int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
compare both
valid? +
match: yes = hit
block offset
short int (2 Bytes) is here
No match:
One line in set is selected for eviction and replacement
Replacement policies: random, least recently used (LRU), …

## Slide 14: 2-Way Set Associative Cache Simulation
M=16 byte addresses, B=2 bytes/block,
S=2 sets, E=2 blocks/set
Address trace (reads, one byte per read):
0 [00002],
1 [00012],
7 [01112],
8 [10002],
0 [00002]
xx
t=2
s=1
b=1
x
x
0
?
?
v
Tag
Block
0
0
0
miss
1
00
M[0-1]
hit
miss
1
01
M[6-7]
miss
1
10
M[8-9]
hit
Set 0
Set 1

## Slide 15: A Higher Level Example
int sum_array_rows(double a[16][16])
{
int i, j;
double sum = 0;
for (i = 0; i < 16; i++)
for (j = 0; j < 16; j++)
sum += a[i][j];
return sum;
}
32 B = 4 doubles
assume: cold (empty) cache,
a[0][0] goes here
int sum_array_rows(double a[16][16])
{
int i, j;
double sum = 0;
for (j = 0; i < 16; i++)
for (i = 0; j < 16; j++)
sum += a[i][j];
return sum;
}
blackboard
Ignore the variables sum, i, j

## Slide 16: Spectrum of Associativity
For a cache with 8 entries

## Slide 17: What about writes?
Multiple copies of data exist:
  L1, L2, Main Memory, Disk
What to do on a write-hit?
  Write-through (write immediately to memory)
  Write-back (defer write to memory until replacement of line)
    Need a dirty bit (line different from memory or not)
What to do on a write-miss?
  Write-allocate (load into cache, update line in cache)
    Good if more writes to the location follow
  No-write-allocate (writes immediately to memory)
Typical
  Write-through + No-write-allocate
  Write-back + Write-allocate

## Slide 18: Intel Core i7 Cache Hierarchy
Regs
L1
d-cache
L1
i-cache
L2 unified cache
Core 0
Regs
L1
d-cache
L1
i-cache
L2 unified cache
Core 3
…
L3 unified cache
(shared by all cores)
Main memory
Processor package
L1 i-cache and d-cache:
  32 KB, 8-way,
  Access: 4 cycles
L2 unified cache:
  256 KB, 8-way,
  Access: 11 cycles
L3 unified cache:
  8 MB, 16-way,
  Access: 30-40 cycles
Block size: 64 bytes for all caches.

## Slide 19: Cache Performance Metrics
Miss Rate
  Fraction of memory references not found in cache (misses / accesses) = 1 – hit rate
  Typical numbers (in percentages):
    3-10% for L1
    can be quite small (e.g., < 1%) for L2, depending on size, etc.
Hit Time
  Time to deliver a line in the cache to the processor
    includes time to determine whether the line is in the cache
  Typical numbers:
    1-2 clock cycle for L1
    5-20 clock cycles for L2
Miss Penalty
  Additional time required because of a miss
    typically 50-200 cycles for main memory (Trend: increasing!)

## Slide 20: Lets think about those numbers
Huge difference between a hit and a miss
  Could be 100x, if just L1 and main memory
Would you believe 99% hits is twice as good as 97%?
  Consider: cache hit time of 1 cycle miss penalty of 100 cycles
  Average access time = hit time + miss rate * miss penalty
  97% hits: 1 cycle + 0.03 * 100 cycles = 4 cycles
  99% hits: 1 cycle + 0.01 * 100 cycles = 2 cycles
This is why “miss rate” is used instead of “hit rate”

## Slide 21: Average memory access time (AMAT)
AMAT = L1hit + PL1miss*(L2hit + PL2miss* Memory)
  Each access costs L1 hit latency
  If L1 misses (PL1miss), then multiply by time to access L2
  Possible to add more cache levels
  Can be specific to instructions or data
Compute AMAT for
  16KB L1 with 95% hit rate, 2 cycle access time
  1MB L2 with 80% hit rate, 20 cycle access time
  Main memory has 200 cycle access time

## Slide 22: Writing Cache Friendly Code
Make the common case go fast
  Focus on the inner loops of the core functions
Minimize the misses in the inner loops
  Repeated references to variables are good (temporal locality)
  Stride-1 reference patterns are good (spatial locality)
Key idea: Our qualitative notion of locality is quantified through our understanding of cache memories.

## Slide 23: Today
Cache organization and operation
Performance impact of caches
  The memory mountain
  Rearranging loops to improve spatial locality
  Using blocking to improve temporal locality

## Slide 24: The Memory Mountain
Read throughput (read bandwidth)
  Number of bytes read from memory per second (MB/s)
Memory mountain: Measured read throughput as a function of spatial and temporal locality.
  Compact way to characterize memory system performance.

## Slide 25: Memory Mountain Test Function
/* The test function */
void test(int elems, int stride) {
int i, result = 0;
volatile int sink;
for (i = 0; i < elems; i += stride)
result += data[i];
sink = result; /* So compiler doesn't optimize away the loop */
}
/* Run test(elems, stride) and return read throughput (MB/s) */
double run(int size, int stride, double Mhz)
{
double cycles;
int elems = size / sizeof(int);
test(elems, stride); /* warm up the cache */
cycles = fcyc2(test, elems, stride, 0); /* call test(elems,stride) */
return (size / stride) / (cycles / Mhz); /* convert cycles to MB/s */
}

## Slide 26: The Memory Mountain
Chart: Stride (x8 bytes)
| s1 | s2 | s3 | s4 | s5 | s6 | s7 | s8 | s9 | s10 | s11 | s12 | s13 | s14 | s15 | s16 | s32 | s64
64M | 4029.59 | 2752.75 | 2159.29 | 1710.75 | 1391.48 | 1176.29 | 1015.77 | 890.72 | 845.57 | 805.46 | 773.78 | 757.94 | 727.91 | 712.66 | 705.63 | 701.98 | 598.19 | 601.22
32M | 4029.36 | 2752.39 | 2160.62 | 1710.98 | 1391.5 | 1176.54 | 1016.71 | 891.8 | 846.98 | 807.22 | 775.18 | 760.41 | 730.74 | 714.98 | 709.26 | 708.88 | 608.99 | 607.39
16M | 4040.1 | 2788.42 | 2188.92 | 1742.97 | 1421.69 | 1201.31 | 1038.37 | 911.7 | 870.39 | 835.31 | 809.25 | 798.05 | 780.28 | 778.37 | 787.2 | 744.13 | 633.53 | 608.86
8M | 4374.01 | 3610.74 | 3002.03 | 2492.39 | 2131.04 | 1821.71 | 1564.14 | 1414.18 | 1404.78 | 1408.59 | 1423.67 | 1456.86 | 1499.61 | 1600.13 | 1667.47 | 1231.7 | 1078.97 | 1026.03
4M | 4642.47 | 4583.8 | 4074.93 | 3557.51 | 3337.59 | 2898.78 | 2535.22 | 2248.83 | 2227.41 | 2203.98 | 2187.29 | 2164.18 | 2156.96 | 2148.52 | 2146.83 | 2131.36 | 2038.29 | 2060.87
2M | 4674.06 | 4659.06 | 4153.1 | 4016.4 | 3540.78 | 3027.05 | 2625.06 | 2321.73 | 2306.4 | 2292.86 | 2282.38 | 2270.35 | 2264.14 | 2259.8 | 2260.46 | 2261.54 | 2224.92 | 2431.58
1M | 4673.77 | 4656.98 | 4156.32 | 4012.65 | 3535.85 | 3021.82 | 2623.08 | 2318.19 | 2303.72 | 2291.55 | 2280.42 | 2270.24 | 2264.82 | 2261.86 | 2261.31 | 2271.41 | 2237.27 | 2432.74
512K | 4673 | 4658.05 | 4267.3 | 4052.55 | 3730.88 | 3236.67 | 2839.93 | 2527.15 | 2513.25 | 2503.12 | 2494.19 | 2517.44 | 2523.1 | 2551.67 | 2555.53 | 2477.41 | 2420.17 | 2590.64
256K | 4672.31 | 4645.58 | 4300.1 | 4091.3 | 3890.2 | 3175.38 | 2748.26 | 2351.27 | 2518.38 | 2627.49 | 2644.71 | 2646.45 | 2690.79 | 2715.46 | 2762.7 | 2445.48 | 2440.11 | 2560.87
128K | 4669.89 | 4661.44 | 4661.75 | 4570.55 | 4453.42 | 4070.1 | 3626.17 | 2349.05 | 3332.47 | 3318.78 | 3328.21 | 3312.1 | 3351.75 | 3197.56 | 3342.59 | 3330.51 | 3335.4 | 3374.9
64K | 4664.69 | 4647.96 | 4646.51 | 4575.1 | 4473.68 | 4218.51 | 3642.61 | 3334.78 | 3395.82 | 3398 | 3403.08 | 3411.87 | 3395.99 | 3299.01 | 4287.45 | 3416.74 | 3389.13 | 3374.16
32K | 4654.62 | 4624.5 | 4631.69 | 4615.62 | 4600.39 | 4585.6 | 4572.8 | 4809.1 | 4803.13 | 4789.7 | 4790.97 | 4784.65 | 4754.23 | 4768.54 | 4750.25 | 4742.01 | 6545.16 | 6408.41
Intel Core i7
32 KB L1 i-cache
32 KB L1 d-cache
256 KB unified L2 cache
8M unified L3 cache
All caches on-chip

## Slide 27: The Memory Mountain
Chart: Stride (x8 bytes)
| s1 | s2 | s3 | s4 | s5 | s6 | s7 | s8 | s9 | s10 | s11 | s12 | s13 | s14 | s15 | s16 | s32 | s64
64M | 4029.59 | 2752.75 | 2159.29 | 1710.75 | 1391.48 | 1176.29 | 1015.77 | 890.72 | 845.57 | 805.46 | 773.78 | 757.94 | 727.91 | 712.66 | 705.63 | 701.98 | 598.19 | 601.22
32M | 4029.36 | 2752.39 | 2160.62 | 1710.98 | 1391.5 | 1176.54 | 1016.71 | 891.8 | 846.98 | 807.22 | 775.18 | 760.41 | 730.74 | 714.98 | 709.26 | 708.88 | 608.99 | 607.39
16M | 4040.1 | 2788.42 | 2188.92 | 1742.97 | 1421.69 | 1201.31 | 1038.37 | 911.7 | 870.39 | 835.31 | 809.25 | 798.05 | 780.28 | 778.37 | 787.2 | 744.13 | 633.53 | 608.86
8M | 4374.01 | 3610.74 | 3002.03 | 2492.39 | 2131.04 | 1821.71 | 1564.14 | 1414.18 | 1404.78 | 1408.59 | 1423.67 | 1456.86 | 1499.61 | 1600.13 | 1667.47 | 1231.7 | 1078.97 | 1026.03
4M | 4642.47 | 4583.8 | 4074.93 | 3557.51 | 3337.59 | 2898.78 | 2535.22 | 2248.83 | 2227.41 | 2203.98 | 2187.29 | 2164.18 | 2156.96 | 2148.52 | 2146.83 | 2131.36 | 2038.29 | 2060.87
2M | 4674.06 | 4659.06 | 4153.1 | 4016.4 | 3540.78 | 3027.05 | 2625.06 | 2321.73 | 2306.4 | 2292.86 | 2282.38 | 2270.35 | 2264.14 | 2259.8 | 2260.46 | 2261.54 | 2224.92 | 2431.58
1M | 4673.77 | 4656.98 | 4156.32 | 4012.65 | 3535.85 | 3021.82 | 2623.08 | 2318.19 | 2303.72 | 2291.55 | 2280.42 | 2270.24 | 2264.82 | 2261.86 | 2261.31 | 2271.41 | 2237.27 | 2432.74
512K | 4673 | 4658.05 | 4267.3 | 4052.55 | 3730.88 | 3236.67 | 2839.93 | 2527.15 | 2513.25 | 2503.12 | 2494.19 | 2517.44 | 2523.1 | 2551.67 | 2555.53 | 2477.41 | 2420.17 | 2590.64
256K | 4672.31 | 4645.58 | 4300.1 | 4091.3 | 3890.2 | 3175.38 | 2748.26 | 2351.27 | 2518.38 | 2627.49 | 2644.71 | 2646.45 | 2690.79 | 2715.46 | 2762.7 | 2445.48 | 2440.11 | 2560.87
128K | 4669.89 | 4661.44 | 4661.75 | 4570.55 | 4453.42 | 4070.1 | 3626.17 | 2349.05 | 3332.47 | 3318.78 | 3328.21 | 3312.1 | 3351.75 | 3197.56 | 3342.59 | 3330.51 | 3335.4 | 3374.9
64K | 4664.69 | 4647.96 | 4646.51 | 4575.1 | 4473.68 | 4218.51 | 3642.61 | 3334.78 | 3395.82 | 3398 | 3403.08 | 3411.87 | 3395.99 | 3299.01 | 4287.45 | 3416.74 | 3389.13 | 3374.16
32K | 4654.62 | 4624.5 | 4631.69 | 4615.62 | 4600.39 | 4585.6 | 4572.8 | 4809.1 | 4803.13 | 4789.7 | 4790.97 | 4784.65 | 4754.23 | 4768.54 | 4750.25 | 4742.01 | 6545.16 | 6408.41
Intel Core i7
32 KB L1 i-cache
32 KB L1 d-cache
256 KB unified L2 cache
8M unified L3 cache
All caches on-chip
Slopes of
spatial
locality

## Slide 28: The Memory Mountain
Chart: Stride (x8 bytes)
| s1 | s2 | s3 | s4 | s5 | s6 | s7 | s8 | s9 | s10 | s11 | s12 | s13 | s14 | s15 | s16 | s32 | s64
64M | 4029.59 | 2752.75 | 2159.29 | 1710.75 | 1391.48 | 1176.29 | 1015.77 | 890.72 | 845.57 | 805.46 | 773.78 | 757.94 | 727.91 | 712.66 | 705.63 | 701.98 | 598.19 | 601.22
32M | 4029.36 | 2752.39 | 2160.62 | 1710.98 | 1391.5 | 1176.54 | 1016.71 | 891.8 | 846.98 | 807.22 | 775.18 | 760.41 | 730.74 | 714.98 | 709.26 | 708.88 | 608.99 | 607.39
16M | 4040.1 | 2788.42 | 2188.92 | 1742.97 | 1421.69 | 1201.31 | 1038.37 | 911.7 | 870.39 | 835.31 | 809.25 | 798.05 | 780.28 | 778.37 | 787.2 | 744.13 | 633.53 | 608.86
8M | 4374.01 | 3610.74 | 3002.03 | 2492.39 | 2131.04 | 1821.71 | 1564.14 | 1414.18 | 1404.78 | 1408.59 | 1423.67 | 1456.86 | 1499.61 | 1600.13 | 1667.47 | 1231.7 | 1078.97 | 1026.03
4M | 4642.47 | 4583.8 | 4074.93 | 3557.51 | 3337.59 | 2898.78 | 2535.22 | 2248.83 | 2227.41 | 2203.98 | 2187.29 | 2164.18 | 2156.96 | 2148.52 | 2146.83 | 2131.36 | 2038.29 | 2060.87
2M | 4674.06 | 4659.06 | 4153.1 | 4016.4 | 3540.78 | 3027.05 | 2625.06 | 2321.73 | 2306.4 | 2292.86 | 2282.38 | 2270.35 | 2264.14 | 2259.8 | 2260.46 | 2261.54 | 2224.92 | 2431.58
1M | 4673.77 | 4656.98 | 4156.32 | 4012.65 | 3535.85 | 3021.82 | 2623.08 | 2318.19 | 2303.72 | 2291.55 | 2280.42 | 2270.24 | 2264.82 | 2261.86 | 2261.31 | 2271.41 | 2237.27 | 2432.74
512K | 4673 | 4658.05 | 4267.3 | 4052.55 | 3730.88 | 3236.67 | 2839.93 | 2527.15 | 2513.25 | 2503.12 | 2494.19 | 2517.44 | 2523.1 | 2551.67 | 2555.53 | 2477.41 | 2420.17 | 2590.64
256K | 4672.31 | 4645.58 | 4300.1 | 4091.3 | 3890.2 | 3175.38 | 2748.26 | 2351.27 | 2518.38 | 2627.49 | 2644.71 | 2646.45 | 2690.79 | 2715.46 | 2762.7 | 2445.48 | 2440.11 | 2560.87
128K | 4669.89 | 4661.44 | 4661.75 | 4570.55 | 4453.42 | 4070.1 | 3626.17 | 2349.05 | 3332.47 | 3318.78 | 3328.21 | 3312.1 | 3351.75 | 3197.56 | 3342.59 | 3330.51 | 3335.4 | 3374.9
64K | 4664.69 | 4647.96 | 4646.51 | 4575.1 | 4473.68 | 4218.51 | 3642.61 | 3334.78 | 3395.82 | 3398 | 3403.08 | 3411.87 | 3395.99 | 3299.01 | 4287.45 | 3416.74 | 3389.13 | 3374.16
32K | 4654.62 | 4624.5 | 4631.69 | 4615.62 | 4600.39 | 4585.6 | 4572.8 | 4809.1 | 4803.13 | 4789.7 | 4790.97 | 4784.65 | 4754.23 | 4768.54 | 4750.25 | 4742.01 | 6545.16 | 6408.41
Intel Core i7
32 KB L1 i-cache
32 KB L1 d-cache
256 KB unified L2 cache
8M unified L3 cache
All caches on-chip
Slopes of
spatial
locality
Ridges of
Temporal
locality

## Slide 29: Today
Cache organization and operation
Performance impact of caches
  The memory mountain
  Rearranging loops to improve spatial locality
  Using blocking to improve temporal locality

## Slide 30: Miss Rate Analysis for Matrix Multiply
Assume:
  Line size = 32B (big enough for four 64-bit words)
  Matrix dimension (N) is very large
    Approximate 1/N as 0.0
  Cache is not even big enough to hold multiple rows
Analysis Method:
  Look at access pattern of inner loop
A
k
i
B
k
j
C
i
j

## Slide 31: Matrix Multiplication Example
Description:
  Multiply N x N matrices
  O(N3) total operations
  N reads per source element
  N values summed per destination
    but may be able to hold in register
/* ijk */
for (i=0; i<n; i++) {
for (j=0; j<n; j++) {
sum = 0.0;
for (k=0; k<n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum;
}
}
Variable sum
held in register

## Slide 32: Layout of C Arrays in Memory (review)
C arrays allocated in row-major order
  each row in contiguous memory locations
Stepping through columns in one row:
  for (i = 0; i < N; i++)
    sum += a[0][i];
  accesses successive elements
  if block size (B) > 4 bytes, exploit spatial locality
    compulsory miss rate = 4 bytes / B
Stepping through rows in one column:
  for (i = 0; i < n; i++)
    sum += a[i][0];
  accesses distant elements
  no spatial locality!
    compulsory miss rate = 1 (i.e. 100%)

## Slide 33: Matrix Multiplication (ijk)
/* ijk */
for (i=0; i<n; i++) {
for (j=0; j<n; j++) {
sum = 0.0;
for (k=0; k<n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum;
}
}
A
B
C
(i,*)
(*,j)
(i,j)
Inner loop:
Column-
wise
Row-wise
Fixed
Misses per inner loop iteration:
  A B C
  0.25 1.0 0.0

## Slide 34: Matrix Multiplication (jik)
/* jik */
for (j=0; j<n; j++) {
for (i=0; i<n; i++) {
sum = 0.0;
for (k=0; k<n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum
}
}
A
B
C
(i,*)
(*,j)
(i,j)
Inner loop:
Row-wise
Column-
wise
Fixed
Misses per inner loop iteration:
  A B C
  0.25 1.0 0.0

## Slide 35: Matrix Multiplication (kij)
/* kij */
for (k=0; k<n; k++) {
for (i=0; i<n; i++) {
r = a[i][k];
for (j=0; j<n; j++)
c[i][j] += r * b[k][j];
}
}
A
B
C
(i,*)
(i,k)
(k,*)
Inner loop:
Row-wise
Row-wise
Fixed
Misses per inner loop iteration:
  A B C
  0.0 0.25 0.25

## Slide 36: Matrix Multiplication (ikj)
/* ikj */
for (i=0; i<n; i++) {
for (k=0; k<n; k++) {
r = a[i][k];
for (j=0; j<n; j++)
c[i][j] += r * b[k][j];
}
}
A
B
C
(i,*)
(i,k)
(k,*)
Inner loop:
Row-wise
Row-wise
Fixed
Misses per inner loop iteration:
  A B C
  0.0 0.25 0.25

## Slide 37: Matrix Multiplication (jki)
/* jki */
for (j=0; j<n; j++) {
for (k=0; k<n; k++) {
r = b[k][j];
for (i=0; i<n; i++)
c[i][j] += a[i][k] * r;
}
}
A
B
C
(*,j)
(k,j)
Inner loop:
(*,k)
Column-
wise
Column-
wise
Fixed
Misses per inner loop iteration:
  A B C
  1.0 0.0 1.0

## Slide 38: Matrix Multiplication (kji)
/* kji */
for (k=0; k<n; k++) {
for (j=0; j<n; j++) {
r = b[k][j];
for (i=0; i<n; i++)
c[i][j] += a[i][k] * r;
}
}
A
B
C
(*,j)
(k,j)
Inner loop:
(*,k)
Fixed
Column-
wise
Column-
wise
Misses per inner loop iteration:
  A B C
  1.0 0.0 1.0

## Slide 39: Summary of Matrix Multiplication
ijk (& jik):
  2 loads, 0 stores
  misses/iter = 1.25
kij (& ikj):
  2 loads, 1 store
  misses/iter = 0.5
jki (& kji):
  2 loads, 1 store
  misses/iter = 2.0
for (i=0; i<n; i++) {
for (j=0; j<n; j++) {
sum = 0.0;
for (k=0; k<n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum;
}
}
for (k=0; k<n; k++) {
for (i=0; i<n; i++) {
r = a[i][k];
for (j=0; j<n; j++)
c[i][j] += r * b[k][j];
}
}
for (j=0; j<n; j++) {
for (k=0; k<n; k++) {
r = b[k][j];
for (i=0; i<n; i++)
c[i][j] += a[i][k] * r;
}
}

## Slide 40: Core i7 Matrix Multiply Performance
Chart: Array size (n)
| 50 | 100 | 150 | 200 | 250 | 300 | 350 | 400 | 450 | 500 | 550 | 600 | 650 | 700 | 750
jki | 6.4 | 6.87 | 4.14 | 5.53 | 10.93 | 33.23 | 49.43 | 51.49 | 52.06 | 52.06 | 52.07 | 52.09 | 52.12 | 52.17 | 52.2
kji | 6.4 | 6.82 | 4.01 | 5.33 | 11.04 | 33.21 | 49.42 | 51.5 | 52.07 | 52.08 | 52.09 | 52.1 | 52.14 | 52.19 | 52.23
ijk | 5.31 | 6.35 | 6.29 | 3.7 | 3.72 | 3.71 | 3.72 | 3.83 | 4.6 | 7.74 | 11.71 | 16.54 | 20.57 | 23.85 | 23.86
jik | 5.4 | 6.23 | 3.64 | 3.71 | 3.61 | 3.6 | 3.63 | 3.74 | 4.64 | 7.57 | 11.62 | 16.44 | 20.44 | 23.68 | 23.66
kij | 4.37 | 5.36 | 3.23 | 3.32 | 3.29 | 3.24 | 3.2 | 3.17 | 3.16 | 3.14 | 3.13 | 3.12 | 3.1 | 3.1 | 3.08
ikj | 3.58 | 5.31 | 3.19 | 3.18 | 3.15 | 3.12 | 3.1 | 3.1 | 3.11 | 3.09 | 3.07 | 3.06 | 3.02 | 3.02 | 3.01
jki / kji
ijk / jik
kij / ikj

## Slide 41: Today
Cache organization and operation
Performance impact of caches
  The memory mountain
  Rearranging loops to improve spatial locality
  Using blocking to improve temporal locality

## Slide 42: Example: Matrix Multiplication
a
b
i
j
*
c
=
c = (double *) calloc(sizeof(double), n*n);
/* Multiply n x n matrices a and b */
void mmm(double *a, double *b, double *c, int n) {
int i, j, k;
for (i = 0; i < n; i++)
for (j = 0; j < n; j++)
for (k = 0; k < n; k++)
c[i*n+j] += a[i*n + k]*b[k*n + j];
}

## Slide 43: Cache Miss Analysis
Assume:
  Matrix elements are doubles
  Cache block = 8 doubles
  Cache size C << n (much smaller than n)
First iteration:
  n/8 + n = 9n/8 misses
  Afterwards in cache: (schematic)
*
=
n
*
=
8 wide

## Slide 44: Cache Miss Analysis
Assume:
  Matrix elements are doubles
  Cache block = 8 doubles
  Cache size C << n (much smaller than n)
Second iteration:
  Again: n/8 + n = 9n/8 misses
Total misses:
  9n/8 * n2 = (9/8) * n3
n
*
=
8 wide

## Slide 45: Blocked Matrix Multiplication
c = (double *) calloc(sizeof(double), n*n);
/* Multiply n x n matrices a and b */
void mmm(double *a, double *b, double *c, int n) {
int i, j, k;
for (i = 0; i < n; i+=B)
for (j = 0; j < n; j+=B)
for (k = 0; k < n; k+=B)
/* B x B mini matrix multiplications */
for (i1 = i; i1 < i+B; i++)
for (j1 = j; j1 < j+B; j++)
for (k1 = k; k1 < k+B; k++)
c[i1*n+j1] += a[i1*n + k1]*b[k1*n + j1];
}
a
b
i1
j1
*
c
=
c
+
Block size B x B

## Slide 46: Cache Miss Analysis
Assume:
  Cache block = 8 doubles
  Cache size C << n (much smaller than n)
  Three blocks fit into cache: 3B2 < C
First (block) iteration:
  B2/8 misses for each block
  2n/B * B2/8 = nB/4 (omitting matrix c)
  Afterwards in cache (schematic)
*
=
*
=
Block size B x B
n/B blocks

## Slide 47: Cache Miss Analysis
Assume:
  Cache block = 8 doubles
  Cache size C << n (much smaller than n)
  Three blocks fit into cache: 3B2 < C
Second (block) iteration:
  Same as first iteration
  2n/B * B2/8 = nB/4
Total misses:
  nB/4 * (n/B)2 = n3/(4B)
*
=
Block size B x B
n/B blocks

## Slide 48: Summary
No blocking: (9/8) * n3
Blocking: 1/(4B) * n3
Suggest largest possible block size B, but limit 3B2 < C!
Reason for dramatic difference:
  Matrix multiplication has inherent temporal locality:
    Input data: 3n2, computation 2n3
    Every array elements used O(n) times!
  But program has to be written properly

## Slide 49: Concluding Observations
Programmer can optimize for cache performance
  How data structures are organized
  How data are accessed
    Nested loop structure
    Blocking is a general technique
All systems favor “cache friendly code”
  Getting absolute optimum performance is very platform specific
    Cache sizes, line sizes, associativities, etc.
  Can get most of the advantage with generic code
    Keep working set reasonably small (temporal locality)
    Use small strides (spatial locality)