## Slide 1
CS:APP2e
CS:APP Chapter 4
Computer Architecture
Instruction Set
Architecture

## Slide 2: Instruction Set Architecture
Assembly Language View
  Processor state
    Registers, memory, …
  Instructions
    addl, pushl, ret, …
    How instructions are encoded as bytes
Layer of Abstraction
  Above: how to program machine
    Processor executes instructions in a sequence
  Below: what needs to be built
    Use variety of tricks to make it run fast
    E.g., execute multiple instructions simultaneously
ISA
Compiler
OS
CPU
Design
Circuit
Design
Chip
Layout
Application
Program

## Slide 3: Y86 Processor State
%eax
%ecx
%edx
%ebx
%esi
%edi
%esp
%ebp
ZF
SF
OF
  Program Registers
    Same 8 as with IA32. Each 32 bits
  Condition Codes
    Single-bit flags set by arithmetic or logical instructions
      ZF: Zero SF:Negative OF: Overflow
  Program Counter
    Indicates address of next instruction
  Program Status
    Indicates either normal operation or some error condition
  Memory
    Byte-addressable storage array
    Words stored in little-endian byte order
RF: Program registers
CC: Condition codes
PC
DMEM: Memory
Stat: Program status

## Slide 4: Y86 Execution
  Sequence of instructions
  PC points to next instruction
  Fetch & decode
    Read instruction at PC
  Execute
    Update registers
    Move values to/from memory
    Update condition codes
  Update PC
    Default: next instruction
    call/jmp instructions set new PC
    goto considered your only option
%eax | %esi
%ecx | %edi
%edx | %esp
%ebx | %ebp
addl %eax, %ecx
irmovl $0x5, %ebx
jmp $0xaddr2
call $0xfn_addr
ZF
SF
OF

## Slide 5: Y86 Instruction Set #1
Byte
0
1
2
3
4
5
pushl rA
A
0
rA
8
jXX Dest
7
fn
Dest
popl rA
B
0
rA
8
call Dest
8
0
Dest
rrmovl rA, rB
cmovXX rA, rB
2
fn
rA
rB
irmovl V, rB
3
0
8
rB
V
rmmovl rA, D(rB)
4
0
rA
rB
D
mrmovl D(rB), rA
5
0
rA
rB
D
OPl rA, rB
6
fn
rA
rB
ret
9
0
nop
1
0
halt
0
0

## Slide 6: Y86 Instructions
Format
  1–6 bytes of information read from memory
    Can determine instruction length from first byte
    Not as many instruction types, and simpler encoding than with IA32
  Each accesses and modifies some part(s) of the program state

## Slide 7: Y86 Instruction Set #2
Byte
0
1
2
3
4
5
pushl rA
A
0
rA
8
jXX Dest
7
fn
Dest
popl rA
B
0
rA
8
call Dest
8
0
Dest
rrmovl rA, rB
cmovXX rA, rB
2
fn
rA
rB
irmovl V, rB
3
0
8
rB
V
rmmovl rA, D(rB)
4
0
rA
rB
D
mrmovl D(rB), rA
5
0
rA
rB
D
OPl rA, rB
6
fn
rA
rB
ret
9
0
nop
1
0
halt
0
0
rrmovl
2
0
cmovle
2
1
cmovl
2
2
cmove
2
3
cmovne
2
4
cmovge
2
5
cmovg
2
6

## Slide 8: Y86 Instruction Set #3
Byte
0
1
2
3
4
5
pushl rA
A
0
rA
8
jXX Dest
7
fn
Dest
popl rA
B
0
rA
8
call Dest
8
0
Dest
rrmovl rA, rB
cmovXX rA, rB
2
fn
rA
rB
irmovl V, rB
3
0
8
rB
V
rmmovl rA, D(rB)
4
0
rA
rB
D
mrmovl D(rB), rA
5
0
rA
rB
D
OPl rA, rB
6
fn
rA
rB
ret
9
0
nop
1
0
halt
0
0
addl
6
0
subl
6
1
andl
6
2
xorl
6
3

## Slide 9: Y86 Instruction Set #4
Byte
0
1
2
3
4
5
pushl rA
A
0
rA
8
jXX Dest
7
fn
Dest
popl rA
B
0
rA
8
call Dest
8
0
Dest
rrmovl rA, rB
cmovXX rA, rB
2
fn
rA
rB
irmovl V, rB
3
0
8
rB
V
rmmovl rA, D(rB)
4
0
rA
rB
D
mrmovl D(rB), rA
5
0
rA
rB
D
OPl rA, rB
6
fn
rA
rB
ret
9
0
nop
1
0
halt
0
0
jmp
7
0
jle
7
1
jl
7
2
je
7
3
jne
7
4
jge
7
5
jg
7
6

## Slide 10: Encoding Registers
Each register has 4-bit ID
  Same encoding as in IA32
Register ID 15 (0xF) indicates “no register”
  Will use this in our hardware design in multiple places
%eax
%ecx
%edx
%ebx
%esi
%edi
%esp
%ebp
0
1
2
3
6
7
4
5

## Slide 11: Instruction Example
Addition Instruction
  Add value in register rA to that in register rB
    Store result in register rB
    Note that Y86 only allows addition to be applied to register data
  Set condition codes based on result
  e.g., addl %eax,%esi Encoding: 60 06
  Two-byte encoding
    First indicates instruction type
    Second gives source and destination registers
addl rA, rB
6
0
rA
rB
Encoded Representation
Generic Form

## Slide 12: Arithmetic and Logical Operations
  Refer to generically as “OPl”
  Encodings differ only by “function code”
    Low-order 4 bytes in first instruction word
  Set condition codes as side effect
addl rA, rB
6
0
rA
rB
subl rA, rB
6
1
rA
rB
andl rA, rB
6
2
rA
rB
xorl rA, rB
6
3
rA
rB
Add
Subtract (rA from rB)
And
Exclusive-Or
Instruction Code
Function Code

## Slide 13: Condition codes
  Set with each arithmetic/logical op.
  ZF: was the result 0?
  SF: was the result <0?
  OF: did the result overflow? (two’s complement)
addl rA, rB
0x1,0x2
0,0,0
instruction
values
ZF,SF,OF
addl rA, rB
TMIN,-1
0,0,1
addl rA, rB
1,-2
0,1,0
addl rA, rB
5,-5
1,0,0
addl rA, rB
TMIN,TMIN
1,0,1

## Slide 14: Move Operations
  Like the IA32 movl instruction
  Simpler format for memory addresses
  Give different names to keep them distinct
rrmovl rA, rB
2
0
rA
rB
Register --> Register
Immediate --> Register
irmovl V, rB
3
0
8
rB
V
Register --> Memory
rmmovl rA, D(rB)
4
0
rA
rB
D
Memory --> Register
mrmovl D(rB), rA
5
0
rA
rB
D

## Slide 15: Move Instruction Examples
irmovl $0xabcd, %edx
movl $0xabcd, %edx
30 82 cd ab 00 00
IA32
Y86
Encoding
rrmovl %esp, %ebx
movl %esp, %ebx
20 43
mrmovl -12(%ebp),%ecx
movl -12(%ebp),%ecx
50 15 f4 ff ff ff
rmmovl %esi,0x41c(%esp)
movl %esi,0x41c(%esp)
—
movl $0xabcd, (%eax)
—
movl %eax, 12(%eax,%edx)
—
movl (%ebp,%eax,4),%ecx
40 64 1c 04 00 00

## Slide 16: Conditional Move Instructions
  Refer to generically as “cmovXX”
  Encodings differ only by “function code”
  Based on values of condition codes
  Variants of rrmovl instruction
    (Conditionally) copy value from source to destination register
rrmovl rA, rB
Move Unconditionally
cmovle rA, rB
Move When Less or Equal
cmovl rA, rB
Move When Less
cmove rA, rB
Move When Equal
cmovne rA, rB
Move When Not Equal
cmovge rA, rB
Move When Greater or Equal
cmovg rA, rB
Move When Greater
2
0
rA
rB
2
1
rA
rB
2
2
rA
rB
2
3
rA
rB
2
4
rA
rB
2
5
rA
rB
2
6
rA
rB

## Slide 17: Jump Instructions
  Refer to generically as “jXX”
  Encodings differ only by “function code”
  Based on values of condition codes
  Same as IA32 counterparts
  Encode full destination address
    Unlike PC-relative addressing seen in IA32
jmp Dest
7
0
Jump Unconditionally
Dest
jle Dest
7
1
Jump When Less or Equal
Dest
jl Dest
7
2
Jump When Less
Dest
je Dest
7
3
Jump When Equal
Dest
jne Dest
7
4
Jump When Not Equal
Dest
jge Dest
7
5
Jump When Greater or Equal
Dest
jg Dest
7
6
Jump When Greater
Dest

## Slide 18: Y86 Program Stack
  Region of memory holding program data
  Used in Y86 (and IA32) for supporting procedure calls
  Stack top indicated by %esp
    Address of top stack element
  Stack grows toward lower addresses
    Bottom element is at highest address in the stack
    When pushing, must first decrement stack pointer
    After popping, increment stack pointer
%esp
•
•
•
Increasing
Addresses
Stack “Top”
Stack “Bottom”

## Slide 19: Stack Operations
  Decrement %esp by 4
  Store word from rA to memory at %esp
  Like IA32
  Read word from memory at %esp
  Save in rA
  Increment %esp by 4
  Like IA32
pushl rA
A
0
rA
F
popl rA
B
0
rA
F

## Slide 20: Subroutine Call and Return
  Push address of next instruction onto stack
  Start executing instructions at Dest
  Like IA32
  Pop value from stack
  Use as address for next instruction
  Like IA32
call Dest
8
0
Dest
ret
9
0

## Slide 21: Miscellaneous Instructions
  Don’t do anything
  Stop executing instructions
  IA32 has comparable instruction, but can’t execute it in user mode
  We will use it to stop the simulator
  Encoding ensures that program hitting memory initialized to zero will halt
nop
1
0
halt
0
0

## Slide 22: Status Conditions
Mnemonic | Code
ADR | 3
Mnemonic | Code
INS | 4
Mnemonic | Code
HLT | 2
Mnemonic | Code
AOK | 1
  Normal operation
  Halt instruction encountered
  Bad address (either instruction or data) encountered
  Invalid instruction encountered
Desired Behavior
  If AOK, keep going
  Otherwise, stop program execution

## Slide 23: Writing Y86 Code
Try to Use C Compiler as Much as Possible
  Write code in C
  Compile for IA32 with gcc34 –O1 –S
    Newer versions of GCC do too much optimization
    Use ls /usr/bin/gcc* to find what versions are available
  Transliterate into Y86
Coding Example
  Find number of elements in null-terminated list
    int len1(int a[]);
5043
6125
7395
0
a
 3

## Slide 24: Y86 Code Generation Example
First Try
  Write typical array code
  Compile with gcc34 –O1 -S
Problem
  Hard to do array indexing on Y86
    Since don’t have scaled addressing modes
/* Find number of elements in
null-terminated list */
int len1(int a[])
{
int len;
for (len = 0; a[len]; len++)
;
return len;
}
L5:
incl %eax
cmpl $0, (%edx,%eax,4)
jne L5

## Slide 25: Y86 Code Generation Example #2
Second Try
  Write with pointer code
  Compile with gcc34 –O1 -S
Result
  Don’t need to do indexed addressing
/* Find number of elements in
null-terminated list */
int len2(int a[])
{
int len = 0;
while (*a++)
len++;
return len;
}
.L11:
incl %ecx
movl (%edx), %eax
addl $4, %edx
testl %eax, %eax
jne .L11

## Slide 26: Y86 Code Generation Example #3
IA32 Code
  Setup
Y86 Code
  Setup
len2:
pushl %ebp
movl %esp, %ebp
movl 8(%ebp), %edx
movl $0, %ecx
movl (%edx), %eax
addl $4, %edx
testl %eax, %eax
je .L13
len2:
pushl %ebp # Save %ebp
rrmovl %esp, %ebp # New FP
pushl %esi # Save
irmovl $4, %esi # Constant 4
pushl %edi # Save
irmovl $1, %edi # Constant 1
mrmovl 8(%ebp), %edx # Get a
irmovl $0, %ecx # len = 0
mrmovl (%edx), %eax # Get *a
addl %esi, %edx # a++
andl %eax, %eax # Test *a
je Done # If zero, goto Done
  Need constants 1 & 4
  Store in callee-save registers
  Use andl to test register

## Slide 27: Y86 Code Generation Example #4
IA32 Code
  Loop
Y86 Code
  Loop
.L11:
incl %ecx
movl (%edx), %eax
addl $4, %edx
testl %eax, %eax
jne .L11
Loop:
addl %edi, %ecx # len++
mrmovl (%edx), %eax # Get *a
addl %esi, %edx # a++
andl %eax, %eax # Test *a
jne Loop # If !0, goto Loop

## Slide 28: Y86 Code Generation Example #5
IA32 Code
  Finish
Y86 Code
  Finish
.L13:
movl %ecx, %eax
leave
ret
Done:
rrmovl %ecx, %eax # return len
popl %edi # Restore %edi
popl %esi # Restore %esi
rrmovl %ebp, %esp # Restore SP
popl %ebp # Restore FP
ret

## Slide 29: Y86 Sample Program Structure #1
  Program starts at address 0
  Must set up stack
    Where located
    Pointer values
    Make sure don’t overwrite code!
  Must initialize data
init: # Initialization
. . .
call Main
halt
.align 4 # Program data
array:
. . .
Main: # Main function
. . .
call len2
. . .
len2: # Length function
. . .
.pos 0x100 # Placement of stack
Stack:

## Slide 30: Y86 Program Structure #2
  Program starts at address 0
  Must set up stack
  Must initialize data
  Can use symbolic names
init:
irmovl Stack, %esp # Set up SP
irmovl Stack, %ebp # Set up FP
call Main # Execute main
halt # Terminate
# Array of 4 elements + terminating 0
.align 4
array:
.long 0x000d
.long 0x00c0
.long 0x0b00
.long 0xa000
.long 0

## Slide 31: Y86 Program Structure #3
Set up call to len2
  Follow IA32 procedure conventions
  Push array address as argument
Main:
pushl %ebp
rrmovl %esp,%ebp
irmovl array,%edx
pushl %edx # Push array
call len2 # Call len2(array)
rrmovl %ebp,%esp
popl %ebp
ret

## Slide 32: Assembling Y86 Program
  Generates “object code” file len.yo
    Actually looks like disassembler output
  unix> yas len.ys
  0x000: | .pos 0
  0x000: 30f400010000 | init: irmovl Stack, %esp # Set up stack pointer
  0x006: 30f500010000 | irmovl Stack, %ebp # Set up base pointer
  0x00c: 8028000000 | call Main # Execute main program
  0x011: 00 | halt # Terminate program
  |
  | # Array of 4 elements + terminating 0
  0x014: | .align 4
  0x014: | array:
  0x014: 0d000000 | .long 0x000d
  0x018: c0000000 | .long 0x00c0
  0x01c: 000b0000 | .long 0x0b00
  0x020: 00a00000 | .long 0xa000
  0x024: 00000000 | .long 0

## Slide 33: Simulating Y86 Program
  Instruction set simulator
    Computes effect of each instruction on processor state
    Prints changes in state from original
  unix> yis len.yo
  Stopped in 50 steps at PC = 0x11. Status 'HLT', CC Z=1 S=0 O=0
  Changes to registers:
  %eax: 0x00000000 0x00000004
  %ecx: 0x00000000 0x00000004
  %edx: 0x00000000 0x00000028
  %esp: 0x00000000 0x00000100
  %ebp: 0x00000000 0x00000100
  Changes to memory:
  0x00ec: 0x00000000 0x000000f8
  0x00f0: 0x00000000 0x00000039
  0x00f4: 0x00000000 0x00000014
  0x00f8: 0x00000000 0x00000100
  0x00fc: 0x00000000 0x00000011

## Slide 34: CISC Instruction Sets
  Complex Instruction Set Computer
  Dominant style through mid-80’s
Stack-oriented instruction set
  Use stack to pass arguments, save program counter
  Explicit push and pop instructions
Arithmetic instructions can access memory
  addl %eax, 12(%ebx,%ecx,4)
    requires memory read and write
    Complex address calculation
Condition codes
  Set as side effect of arithmetic and logical instructions
Philosophy
  Add instructions to perform “typical” programming tasks

## Slide 35: RISC Instruction Sets
  Reduced Instruction Set Computer
  Internal project at IBM, later popularized by Hennessy (Stanford) and Patterson (Berkeley)
Fewer, simpler instructions
  Might take more to get given task done
  Can execute them with small and fast hardware
Register-oriented instruction set
  Many more (typically 32) registers
  Use for arguments, return pointer, temporaries
Only load and store instructions can access memory
  Similar to Y86 mrmovl and rmmovl
No Condition codes
  Test instructions return 0/1 in register

## Slide 36: MIPS Registers

## Slide 37: MIPS Instruction Examples
Op
Ra
Rb
Offset
Op
Ra
Rb
Rd
Fn
00000
R-R
Op
Ra
Rb
Immediate
R-I
Load/Store
addu $3,$2,$1 # Register add: $3 = $2+$1
addu $3,$2, 3145 # Immediate add: $3 = $2+3145
sll $3,$2,2 # Shift left: $3 = $2 << 2
lw $3,16($2) # Load Word: $3 = M[$2+16]
sw $3,16($2) # Store Word: M[$2+16] = $3
Op
Ra
Rb
Offset
Branch
beq $3,$2,dest # Branch when $3 = $2

## Slide 38: CISC vs. RISC
Original Debate
  Strong opinions!
  CISC proponents---easy for compiler, fewer code bytes
  RISC proponents---better for optimizing compilers, can make run fast with simple chip design
Current Status
  For desktop processors, choice of ISA not a technical issue
    With enough hardware, can make anything run fast
    Code compatibility more important
  For embedded processors, RISC makes sense
    Smaller, cheaper, less power
    Most cell phones use ARM processor

## Slide 39: Summary
Y86 Instruction Set Architecture
  Similar state and instructions as IA32
  Simpler encodings
  Somewhere between CISC and RISC
How Important is ISA Design?
  Less now than before
    With enough hardware, can make almost anything go fast
  Intel has evolved from IA32 to x86-64
    Uses 64-bit words (including addresses)
    Adopted some features found in RISC
      More registers (16)
      Less reliance on stack