## Slide 1: Building an Internet Router
Advanced Feature:
Network Address Translation
David Erickson Filip Paun David Chanady
Stanford University
derickso@stanford.edu paun@stanford.edu dchanady@stanford.edu

## Slide 2: What is NAT? Why Use it?
Internet sends data from one location to another, using 32 bit addresses
4,294,967,296 possible addresses
Some reports claim the address space could be fully allocated by 2010*
*http://www.potaroo.net/tools/ipv4/index.html

## Slide 3: High Level Overview
NAT
External Address | External Port | Internal Address | Internal Port
NAT Box | 5385 | David’s Box | 2213
NAT Lookup Table
Src | NAT Box | 5385
Dst | website | 80
Src | David’s Box | 2213
Dst | website | 80
Src | website | 80
Dst | NAT Box | 5385
Src | website | 80
Dst | David’s Box | 2213
David’s Box 2213
website 80

## Slide 4: Our Architecture
Software’s Role – fully functional
  Manage NAT Table Entries
  All ICMP rewriting
  Rewrite any TCP/UDP packets passed from HW
Hardware’s Role – partial functionality
  Check for NAT hit on packets traversing the WAN port
  Rewrite TCP/UDP packets
  Forward misses, ICMP, and unknown types to software

## Slide 5: Hardware Overview (pkt pipeline)
Decode
Route
Update
IN
OUT
Decode: Figure out what to do with the packet
Route: Where should I send this packet?
Update: Make necessary changes before sending

## Slide 6
Hardware Routing (basic router)
IN
Rtable
Lookup
ARP
Lookup
OUT

## Slide 7
Hardware Routing (nat router)
IN
NAT In
Lookup
Rtable
Lookup
ARP
Lookup
OUT
NATOut
Lookup
Non-NAT case
NAT: incoming
NAT: outgoing

## Slide 8: Challenges
ICMP packets
TCP/UDP packet checksum

## Slide 9: ICMP
Type Echo - No port number!
Use the ID field instead!
Echo
Code
Chksum
Seq #
Unique ID

## Slide 10: ICMP
Type Destination Unreachable & Expired TTL
Unwrap the ICMP data payload!
Type
Code
Chksum
Unused
MTU
Data
IP HDR
IP Dst Addr
IP Src Addr
IP SUM
TCP Ports
Dst Port
Src Port

## Slide 11: Checksum
TCP Packets
NAT
NEW_TCP_SUM
OLD_TCP_SUM
Nat Entry: Aux Fields
Ext Sum | Int Sum
X | Y
New_TCP_SUM = OLD_TCP_SUM + X - Y

## Slide 12: Demonstration
TCP (SSH/HTTP)
UDP (Traceroute)
ICMP (Traceroute/Ping)
Most active entry sorting
Entry expiration
PWOSPF Router Interoperability

## Slide 13: Demonstration Topology
Our Router #1
Our Router #2
VNS App Server
Whatismyip.com
DOEmail.stanford.edu
Internet
WAN 171.67.71.61
192.168.130.8/31
192.168.130.14/31