## Slide 1: An Implementation of GEMM for DMA-enabled Architectures Devangi Parikh Will Leven Sep 19, 2016 TI / Embedded Processing / Processors / Silicon Development / Machine Learning Lab
TI Information – Selective Disclosure

## Slide 2: Outline
TI Information – Selective Disclosure
TI Embedded Processors
TI LINALG Library
Application Use Case
GEMM On C66x
Performance

## Slide 3: TI Embedded Processors
TI Information – Selective Disclosure

## Slide 4: 5 Generations of TI Multicore Processors
Keystone architecture
  Lowers development effort
  Speeds time to market
  Leverages TI’s investment
  Optimal software reuse
TI Information – Selective Disclosure

## Slide 5: TI 66AK2H12 SoC
TI Information – Selective Disclosure
Keystone II architecture
Cores
  4 ARM A15s at 1.0 GHz
    4 MB shared L2 cache
    32 Gflops single precision
    8 Gflops double precision
  8 C66x DSPs at 1.0 GHz
    32 kB L1 scratch / cache each
    1 MB L2 scratch / cache each
    128 Gflops single precision
    32 Gflops double precision
Memory
  8 GB DDR3 DRAM (external)
  6 MB shared SRAM/L3
Interfaces

## Slide 6: TI LINALG Library
TI Information – Selective Disclosure

## Slide 7: Dense Linear Algebra
TI Information – Selective Disclosure
LINALG
  Support for the standard CBLAS and CLAPACK APIs
  CBLAS runs on either the available ARM or DSP cores
  Uses BLIS (BLAS-like Library Instantiation Software) for underlying BLAS computations

## Slide 8: Data Movement for Level 3 BLAS on C66x
TI Information – Selective Disclosure
Efficiently moves the input and output matrices through the different levels of memory using DMA, and packing routines to ensure efficient computations
Level 3 BLAS computations require
  4.5 MB MSMC memory
  768 KB L2 Scratchpad memory
  28 KB L1D Scratchpad memory
A
B
C

## Slide 9: Single Precision GEMM Performance
TI Information – Selective Disclosure
Single precision general matrix-matrix multiplication
Obtained using a TI 66AK2H12 SoC at a 1 GHz clock
Theoretical peak DSP performance = 128 GFLOPS
Theoretical peak ARM performance = 32 GFLOPS

## Slide 10: Application Use Case
TI Information – Selective Disclosure

## Slide 11: CNN Applications
TI Information – Selective Disclosure

## Slide 12: Extended BLAS for TIML
TI Information – Selective Disclosure
Input and output final locations (any permutation for the parameters can be provided)
  DRAM
  MSMC / L3
  L2
Fuse GEMM/GEMV with other operations
  Fully connected layer (with or without H pre packed / stored optimally, with or without V special structure)
  Y = ReLU(H*X + V)
  y = ReLU(H*x + v)
  Convolutional layer (with or without H pre packed / stored optimally, with or without V special structure, need to form Xfilter)
  Y = ReLU(H*Xfilter + V)
  Y = pool(ReLU(H*Xfilter + V))
Data movement
  EDMA
Working space
  May assume only L1 is available for scratchpad buffers

## Slide 13: GEMM On C66x
TI Information – Selective Disclosure

## Slide 14: GEMM Building Blocks
TI Information – Selective Disclosure
C66x SGEMM ukernel
  MR_S = 4
  NR_S = 8
  KC_S > 384 (to get > 90% performance from the ukernel)
Packing Routines
  8xK to pack Matrix B
  4xK to pack Matrix A
Memory required for packing
  Available working space 28 KB of L1
  1 micro-panel of B = 12 KB
  1 micro-panel of A = 6 KB

## Slide 15: Performance Analysis
TI Information – Selective Disclosure
  Performance Limitations
    MC and NC have to be very small to fit panels of A and B in L1
    KC has to be reduced to fit more micro-panels of A and B
    Expensive loops (5th loop and 3rd loop around ukernel) iterate large number of times
  Custom Implementation
    GEMM building blocks
      Ukernel (> 90% performance)
    Streamlined Implementation
      Aim to reduce functions calls, and other code generalization
    Use DMA to pack A
      Pack the next micro-panel while computing on current micro-panel
Operations | % of total cycles |  | 
Ukernel | ~42.5 |  | 
Packing A | ~17.2 |  | 
Packing B | ~2.0 |  | 
Overhead | ~38.3 |  | 
M | 256 | MC | 16
N | 256 | NC | 16
K | 198 | KC | 198
 |  | MR | 4
 |  | NR | 8

## Slide 16: GEMM on C66x
TI Information – Selective Disclosure

## Slide 17: Single Precision GEMM Performance
TI Information – Selective Disclosure
Preliminary Results:
Performance (Clock 983 MHz)
  L2 – 11.03 GFLOPS (70 %)
  MSMC – 9.49 GFLOPS (59 %)
Operations | % of total cycles |  | 
Ukernel | ~84.0 |  | 
Packing A | ~7.7 |  | 
Packing B | ~2.7 |  | 
Overhead | ~5.6 |  | 
M | 224 | KC | 398
N | 224 | MR | 4
K | 398 | NR | 8

## Slide 18: Thank you!
TI Information – Selective Disclosure

## Slide 19: Backup
TI Information – Selective Disclosure

## Slide 20: Summary
TI Information – Selective Disclosure
Our previous implementation of Dense Linear Algebra libraries for TI DSP processors assumes all on-chip memory is available as working space to efficiently move data through the various levels of memory using DMA and packing routines. However, this assumption prevents applications from using any on-chip memory to store data that the application may be using frequently. In this talk, we will describe an implementation of GEMM that uses a limited amount of working space, and DMAs to pack matrices freeing up most of the on-chip memory for the applications’ use.