## Slide 1: Traffic Optimization For a Mixture of Self-interested and Compliant Agents
Guni Sharon, Michael Albert, Tarun Rambha, Stephen Boyles and Peter Stone

## Slide 2: Overview
Route a flow of agents across a network
S
T

## Slide 3: Overview
Route a flow of agents across a network
Self interested routing → user equilibrium
S
T

## Slide 4: Overview
S
T
Route a flow of agents across a network
Self interested routing → user equilibrium
System optimum routing → optimal flow
Least marginal cost path

## Slide 5: Overview
Route a flow of agents across a network
Self interested routing → user equilibrium
System optimum routing → optimal flow
Mixed, SO-UE scenario → ?
S
T
?

## Slide 6: Mixed UE-SO equilibrium
Mixed scenario is a Stackelberg game
SO agents are the leaders
UE agents are the followers
S
T
SO
UE

## Slide 7: Motivation
Influencing self interested agents is expensive
A system manager usually has limited resources

## Slide 8: Problem definition
Given:
  A network
  A set of latency functions
    non-negative, differentiable, non-decreasing, convex
  The demand for each source target pair
Return:
  The minimal set of SO agents that is required in order to achieve SO flow?
1 → 9 : 12 agents
5 → 12 : 4 agents
…
: agents

## Slide 9: Related work
Equilibrium for a mixed UE, Cournot-Nash (CN) scenario
  Unique, can be computed using a convex program
    (Haurie and Marcotte 1985; Yang and Zhang 2008)
  Equilibrium for a mixed UE, SO scenario with common source and a common target and any number of parallel links
  Korilis et. al. (1997)
  NP-hard in the general case (Roughgarden 2004)
S
T

## Slide 10: Example problem
= the latency on link as a function of the assigned flow
Assume demand:
  1 → 3 :
  3 → 5 :
  2 → 4 : 1
  Else : 0

## Slide 11: System optimum
What routes would a self interested agent consider?

## Slide 12: System optimum
What routes would a self interested agent consider?
The least latency routes!
  1 → 3 :
  3 → 5 :
  2 → 4 : →

## Slide 13: Self interested sub-flow
Self interested flow may be assigned only to least latency path
Self interested flow may not exceed the flow at SO
Run max-flow under these constraint and the original demand

## Slide 14: Self interested sub-flow
Self interested flow may be assigned only to lease latency path
Self interested flow may not exceed the flow at SO
Run max-flow under these constraint and the original demand
Wrong!
We are missing a constraint

## Slide 15: Missing a constraint
The previous solution assigns a flow of 1 to the dashed link
At SO no flow originating from 1 or 3 may travel the dotted line
At SO no flow originating from 2 may travel the dotted line

## Slide 16: Another necessary constraint
Self-interested flow must follow SO paths
  Paths with least marginal cost
Run max-flow under these constraint and the original demand

## Slide 17: LP formalization
Maximize the self-interested flow over all source-target pairs
Self interested flow may not exceed original demand
Flow originate at source
Flow preservation constraint
Self-interested flow may not exceed flow at SO solution
No negative flow or demand
Positive flow is assigned only to paths with minimal latency and minimal marginal cost

## Slide 18: Proof of correctness

## Slide 19: Experimental results
Six benchmark traffic scenarios, available at: https://github.com/bstabler/
Smaller networks can tolerate more self-interested agents at SO
  Larger networks -> less zero reduced paths -> less self-interested agents
Scenario | Vertices | Links | Total demand | UE TTT | SO TTT | % improvement | % self-interested
Sioux Falls | 24 | 76 | 360,600 | 7,480,225 | 7,194,256 | 3.82 | 86.96
Eastern MA | 74 | 258 | 65,576 | 28,181 | 27,323 | 3.04 | 80.27
Anaheim | 416 | 914 | 104,694 | 1,419,913 | 1,395,015 | 1.75 | 80.24
Chicago | 933 | 2,950 | 1,260,907 | 18,377,329 | 17,953,267 | 2.31 | 72.71
Philadelphia | 13,389 | 40,003 | 18,503,872 | 335,647,106 | 324,268,465 | 3.39 | 50.41
Chicago regional | 12,982 | 39,018 | 1,360,427 | 33,656,964 | 31,942,956 | 5.09 | 46.66

## Slide 20: Take home
Achieving optimal traffic flow might not require controlling all agents
The paper presents a tractable LP for computing the maximal volume of self-interested agents that a system can tolerate at SO
The LP solution identifies the set of required SO agents
The paper also provides answers to the following:
  What routes should be assigned to the SO agents?
  Is a given set of SO agents sufficient for achieving SO flow?