## Slide 1: Cloaking Malware with the Trusted Platform Module
Alan Dunn, Owen Hofmann,
Brent Waters, Emmett Witchel
University of Texas at Austin
USENIX Security
August 12, 2011

## Slide 2: Trusted Computing
Goal: Secure environment for computation
Trust rooted in hardware
Most familiar: Trusted Platform Module (TPM)
  Standard by Trusted Computing Group (TCG)
  IC in x86 machines connected to southbridge
  Widely deployed (> 350 million TPMs)

## Slide 3: Uses of Trusted Computing
Typical: TPM provides hardware root of trust
  Store cryptographic hash of executed software
  Perform cryptography, store secret keys
  Provide hardware-protected execution environment
Ours: TPM provides hardware cloak for malware
  Only run unmodified malware
  Store malware secret keys
  No monitoring/debuggers/virtualization
Notes: Mention BitLocker, mention here specifically again that we are inverting the normal way we go about looking at security properties
Change this to “TPM and late launch”? It is technically incorrect as is (the TPM itself doesn’t do anything w.r.t. protecting execution)
I have the ordering now such that the last three points do not mirror the first three, but it seems like a weird order to run them in if I do…

## Slide 4: Conficker B Explanation
get_updates()
gen_domains()
date = get_date_from_web()
calculate domains…
for domain in domains:
content = fetch_content(domains)
if (check_sig(content))
apply_update(content)
!
Contact websites
www.google.com
aijuer.com
lkpexhjz.org…
“8/13/11”
“8/12/11”
Goal for malware writers: Secure and hidden malware sub-computation
Secure date mechanism
Conficker B Analysis
TPM can help malware writers achieve this goal:
Execute computation securely in non-analyzable environment
Notes: Motivate the weird domain names

## Slide 5: Outline
Protocol Overview
Protocol
Implementation
Defenses

## Slide 6: Protocol Overview
Late launch environment
Infected Platform
Malware Distribution Platform
(MDP)
Put platform in known non-analyzable state
Restrict payload decryption to non-analyzable state
Infection
Payload Loader
main()
…
sensitive_calc()
…
normal_calc()
…
sensitive_calc()
…

## Slide 7: Put platform in non-analyzable state
Suspend all system software, jump into known software state
Late launch performs jump, records program jumped to via hash
Infected Platform
Late launch environment
Infection
Payload Loader
Notes: Stay higher-level here…

## Slide 8: Restricting payload decryption
TPM controls private key use for keypairs it generates
Binding key constrained to use in non-analyzable state
Certificates show Endorsement Key (EK) belongs to legitimate TPM
Remote attestation proves binding key generated by same party as EK, so payload only decryptable in late launch
Infected Platform
Malware Distribution Platform
(MDP)
Binding key
Malicious payload
Notes: Add binding key into the picture?

## Slide 9: Late Launch
SENTER instruction transfers control to binary, sets TPM register based upon cryptographic hash of binary
  Allows binary to execute securely: stop other cores, turn off interrupts
For malware:
  Transfer control to Infection Payload Loader (IPL)
  IPL hash satisfies key use constraint
  IPL decrypts, transfers control to malicious payload
Notes: Put enough here so that we can describe difficulties of the malware computation model later in more detail with the Conficker example

## Slide 10: Validating the Binding Key
Endorsement Key (EK) – unique identifying key, certified by TPM manufacturer
Sign(EK, M1)
Sign(EK, M2)
Correlate transactions
A
P1
P2
Sign binding key with EK? Forbidden!
EK identifying, compromises anonymity
Notes: Make note somewhere on slide that this is used for key authenticity?
Rejigger this in combination with the next slide, e.g. ensure people realize that one of these two diagrams “transforms” into the next

## Slide 11: TPM Identity (EK) with Indirection (AIK)
Attestation Identity Keys (AIKs) fix anonymity
Privacy CA vouches that AIK represents EK
Sign(AIK1, M1)
Sign(AIK2, M2)
A
P1
P2
C
Establish EK legitimacy,
AIKs proxy for EK
C vouches for legitimacy of AIKs
C is a Privacy CA
Problem: Privacy CAs don’t exist
Solution: Malware Distribution Platform acts as Privacy CA

## Slide 12: Can malware generate an AIK?
Owner AuthData required for AIK generation
Owner AuthData not needed on platform, used rarely
Capture from keylogging or from memory (Windows: cached for days)
Notes: Do explain what AuthData is
Removed point: AuthData not transmitted to TPM

## Slide 13: Remote attestation details
Infected Platform
Malware Distribution Platform
(MDP)
2) PKEK, PKAIK, Sign(SKmanuf.,H(PKEK))
4) Enc(PKEK, cred || H(PKAIK))
Phase 1: cred  AIK represents EK
1) Generate AIK
5) Activate AIK: if H(PKAIK) matches AIK generated on that platform, TPM releases cred
3) Verify EK sig
Notes: Put cred as signed H(PKAIK) as in paper? Sounds like “no” from audience feedback

## Slide 14: Remote attestation details (cont’d)
2) PKbind, key use constraint, cred, Sign(SKAIK,H(PKbind||key use constraint))
Phase 2: Prove binding key is from TPM that controls EK
1) Generate binding key with use constraint
3) Verify use constraint, cred
Infected Platform
Malware Distribution Platform
(MDP)
4) Send encrypted malicious payload
Malicious payload
5) Late launch, decrypt and run payload
Notes: See prior slide comments
Try it one time with the actual payload decryption and launch

## Slide 15: Implementation
Protocol until late launch (w/TrouSerS)
Late launch (via Flicker v0.2) on Intel platforms
  Infection Payload Loader (IPL): decrypt, execute payload
  IPL run appears as 3 second system freeze on Infected Platform due to TPM key operations in late launch
Three malicious payloads
  Conficker B-like example
    Secure time via Ubuntu package manifests
  DDoS timebomb
  Secret text search
Notes: More performance measurements in paper
Say: “That’s all about performance measurments”, mention payloads run at native performance
Mention Ubuntu package manifests here?

## Slide 16: Defense: Whitelisting late launch binaries
Hypervisor-level whitelisting
  Trap on SENTER, check late launch binary
    List of hashes of whitelisted binaries
    Digitally sign binaries, whitelist signing keys
Problems
  Requires hypervisor: tough for home users
  Late launch binary updates
  Signatures: Revocation, trust management (certificate chains)
Notes:   Middle point used to say:
  Configuration management
    Ensuring all important data captured in hash
    Late launch binary updates

## Slide 17: Defense: Manufacturer Cooperation
Manufacturer breaks TPM guarantees for analyst
Fake Endorsement Key (EK)
  Manufacturer produces certificate for EK that is not TPM controlled
  Problem: EK leak can compromise TPM security properties
Fake Attestation Identity Key (AIK)
  Manufacturer uses EK to complete AIK activation for AIK that is not TPM controlled
  Problem: AIK requests need manufacturer response online

## Slide 18: Defense: Physical Compromises
TPM compromise has been demonstrated
  Simple: Grounding LPC bus allowed faking of TPM code measurement
  Exotic: Etching away casing, probing around tamper-resistant wiring allowed EK recovery
Industry incentives to fix
Further discussion in paper (e.g. cold boot)

## Slide 19: Conclusion
TPM can cloak malware sub-computations, hiding them from analysts
Concrete implementation of TPM-based malware cloaking
  Remote attestation
  Late launch
Strengthening TPM guarantees makes attack more resilient
Notes: Ending should talk about the Catch-22 re: defenses