## Slide 1: BLIS Matrix Multiplication: from Real to Complex
Field G. Van Zee

## Slide 2: Acknowledgements
Funding
  NSF Award OCI-1148125: SI2-SSI: A Linear Algebra Software Infrastructure for Sustained Innovation in Computational Chemistry and other Sciences. (Funded June 1, 2012 - May 31, 2015.)
  Other sources (Intel, Texas Instruments)
Collaborators
  Tyler Smith, Tze Meng Low

## Slide 3: Acknowledgements
Journal papers
  “BLIS: A Framework for Rapid Instantiation of BLAS Functionality” (accepted to TOMS)
  “The BLIS Framework: Experiments in Portability” (accepted to TOMS pending minor modifications)
  “Analytical Modeling is Enough for High Performance BLIS” (submitted to TOMS)
Conference papers
  “Anatomy of High-Performance Many-Threaded Matrix Multiplication” (accepted to IPDPS 2014)

## Slide 4: Introduction
Before we get started…
  Let’s review the general matrix-matrix multiplication (gemm) as implemented by Kazushige Goto in GotoBLAS. [Goto and van de Geijn 2008]

## Slide 5: The gemm algorithm
+=

## Slide 6: The gemm algorithm
+=
NC
NC

## Slide 7: The gemm algorithm
+=

## Slide 8: The gemm algorithm
+=
KC
KC

## Slide 9: The gemm algorithm
+=

## Slide 10: The gemm algorithm
+=
Pack row panel of B

## Slide 11: The gemm algorithm
+=
Pack row panel of B
NR

## Slide 12: The gemm algorithm
+=

## Slide 13: The gemm algorithm
+=
MC

## Slide 14: The gemm algorithm
+=

## Slide 15: The gemm algorithm
+=
Pack block of A

## Slide 16: The gemm algorithm
+=
Pack block of A
MR

## Slide 17: The gemm algorithm
+=

## Slide 18: Where the micro-kernel fits in
Macro-kernel consists of three loops (cache block sizes)
  NC dimension
  MC dimension
  KC dimension
+=
for ( 0 to NC-1 )
for ( 0 to MC-1 )
for ( 0 to KC-1 )
// outer product
endfor
endfor
endfor
NC
KC
MC

## Slide 19: Where the micro-kernel fits in
+=
for ( 0 to NC-1 )
for ( 0 to MC-1 )
for ( 0 to KC-1 )
// outer product
endfor
endfor
endfor

## Slide 20: Where the micro-kernel fits in
+=
NR
NR
for ( 0 to NC-1: NR )
for ( 0 to MC-1 )
for ( 0 to KC-1 )
// outer product
endfor
endfor
endfor

## Slide 21: Where the micro-kernel fits in
+=
for ( 0 to NC-1: NR )
for ( 0 to MC-1 )
for ( 0 to KC-1 )
// outer product
endfor
endfor
endfor

## Slide 22: Where the micro-kernel fits in
MR
+=
MR
for ( 0 to NC-1: NR )
for ( 0 to MC-1: MR )
for ( 0 to KC-1 )
// outer product
endfor
endfor
endfor

## Slide 23: Where the micro-kernel fits in
+=
for ( 0 to NC-1: NR )
for ( 0 to MC-1: MR )
for ( 0 to KC-1 )
// outer product
endfor
endfor
endfor

## Slide 24: The gemm micro-kernel
+=
KC
NR
MR
NR
C
A
B
for ( 0 to NC-1: NR )
for ( 0 to MC-1: MR )
for ( 0 to KC-1 )
// outer product
endfor
endfor
endfor

## Slide 25: The gemm micro-kernel
C
+=
KC
NR
MR
NR
α1
α2
α3
α0
β1
β0
β2
β3
γ00
γ10
γ20
γ30
γ01
γ11
γ21
γ31
γ02
γ12
γ22
γ32
γ03
γ13
γ23
γ33
+=
A
B
for ( 0 to NC-1: NR )
for ( 0 to MC-1: MR )
for ( 0 to KC-1: 1 )
// outer product
endfor
endfor
endfor
Typical micro-kernel loop iteration
  Load column of packed A
  Load row of packed B
  Compute outer product
  Update C (kept in registers)

## Slide 26: From real to complex
HPC community focuses on real domain. Why?
  Prevalence of real domain applications
  Benchmarks
  Complex domain has unique challenges

## Slide 27: From real to complex
HPC community focuses on real domain. Why?
  Prevalence of real domain applications
  Benchmarks
  Complex domain has unique challenges

## Slide 28: Challenges
Programmability
Floating-point latency / register set size
Instruction set

## Slide 29: Challenges
Programmability
Floating-point latency / register set size
Instruction set

## Slide 30: Programmability
What do you mean?
  Programmability of BLIS micro-kernel
  Micro-kernel typically must be implemented in assembly language
Ugh. Why assembly?
  Compilers have trouble efficiently using vector instructions
  Even using vector instrinsics tends to leave flops on the table

## Slide 31: Programmability
Okay fine, I’ll write my micro-kernel in assembly. It can’t be that bad, right?
  I could show you actual assembly code, but…
  This is supposed to be a retreat!
  Diagrams are more illustrative anyway

## Slide 32: Programmability
Diagrams will depict rank-1 update. Why?
  It’s the body of the micro-kernel’s loop!
Instruction set
  Similar to Xeon Phi
Notation
  α, β, γ are elements of matrices A, B, C, respectively
Let’s begin with the real domain

## Slide 33: Real rank-1 update in assembly
β1
β0
β2
β3
β0
β0
β0
β0
bcast
β1
β1
β1
β1
β2
β2
β2
β2
β3
β3
β3
β3
α1
α2
α3
α0
load
add
αβ00
αβ10
αβ30
αβ20
αβ01
αβ11
αβ31
αβ21
αβ02
αβ12
αβ32
αβ22
αβ03
αβ13
αβ33
αβ23
γ00
γ10
γ30
γ20
γ01
γ11
γ31
γ21
γ02
γ12
γ32
γ22
γ03
γ13
γ33
γ23
mul
α0
α1
α3
α2
4 elements per vector register
Implements 4 x 4 rank-1 update
α0:3 , β0:3 are real elements
Load/swizzle instructions req’d:
  Load
  Broadcast
Floating-point instructions req’d:
  Multiply
  Add

## Slide 34: Complex rank-1 update in assembly
4 elements per vector register
Implements 2 x 2 rank-1 update
α0+iα1 , α2+iα3 , β0+iβ1 , β2+iβ3 are complex elements
Load/swizzle instructions req’d:
  Load
  Duplicate
  Shuffle (within “lanes”)
  Permute (across “lanes”)
Floating-point instructions req’d:
  Multiply
  Add
  Subadd
High values in micro-tile still need to be swapped (after loop)
subadd
β0
β0
β2
β2
β1
β1
β3
β3
β2
β2
β0
β0
β3
β3
β1
β1
load
αβ00
αβ10
αβ32
αβ22
αβ11
αβ01
αβ23
αβ33
αβ02
αβ12
αβ30
αβ20
αβ13
αβ03
αβ21
αβ31
γ00
γ10
γ31
γ21
γ01
γ11
γ30
γ20
α0
α1
α3
α2
α1
α0
α2
α3
shuf
dup
dup
perm
perm
mul
αβ00‒αβ11
αβ10+αβ01
αβ32+αβ23
αβ22‒αβ33
αβ02‒αβ13
αβ12+αβ03
αβ30+αβ21
αβ20‒αβ31
add
α1
α2
α3
α0
β1
β0
β2
β3

## Slide 35: Programmability
Bottom line
  Expressing complex arithmetic in assembly
    Awkward (at best)
    Tedious (potentially error-prone)
    May not even be possible if instructions are missing!
    Or may be possible but at lower performance (flop rate)
  Assembly-coding real domain isn’t looking so bad now, is it?

## Slide 36: Challenges
Programmability
Floating-point latency / register set size
Instruction set

## Slide 37: Latency / register set size
Complex rank-1 update needs extra registers to hold intermediate results from “swizzle” instructions
  But that’s okay! I can just reduce MR x NR (micro-tile footprint) because complex does four times as many flops!
  Not quite: four times flops on twice data
  Hrrrumph. Okay fine, twice as many flops per byte

## Slide 38: Latency / register set size
Actually, this two-fold flops-per-byte advantage for complex buys you nothing
  Wait, what? Why?

## Slide 39: Latency / register set size
What happened to my extra flops!?
  They’re still there, but there is a problem…

## Slide 40: Latency / register set size
What happened to my extra flops!?
  They’re still there, but there is a problem…

## Slide 41: Latency / register set size
What happened to my extra flops!?
  They’re still there, but there is a problem…
  Each element γ must be updated TWICE

## Slide 42: Latency / register set size
What happened to my extra flops!?
  They’re still there, but there is a problem…
  Each element γ must be updated TWICE

## Slide 43: Latency / register set size
What happened to my extra flops!?
  They’re still there, but there is a problem…
  Each element γ must be updated TWICE

## Slide 44: Latency / register set size
What happened to my extra flops!?
  They’re still there, but there is a problem…
  Each element γ must be updated TWICE
    Complex rank-1 update = TWO real rank-1 updates

## Slide 45: Latency / register set size
What happened to my extra flops!?
  They’re still there, but there is a problem…
  Each element γ must be updated TWICE
    Complex rank-1 update = TWO real rank-1 updates
  Each update of γ still requires a full latency period

## Slide 46: Latency / register set size
What happened to my extra flops!?
  They’re still there, but there is a problem…
  Each element γ must be updated TWICE
    Complex rank-1 update = TWO real rank-1 updates
  Each update of γ still requires a full latency period
  Yes, we get to execute twice as many flops, but we are forced to spend twice as long executing them!

## Slide 47: Latency / register set size
So I have to keep MR x NR the same?
  Probably, yes (in bytes)
And I still have to find registers to swizzle?
  Yes

## Slide 48: Latency / register set size
So I have to keep MR x NR the same?
  Probably, yes (in bytes)
And I still have to find registers to swizzle?
  Yes
RvdG
  “This is why I like to live my life as a double.”

## Slide 49: Challenges
Programmability
Floating-point latency / register set size
Instruction set

## Slide 50: Instruction set
Need more sophisticated swizzle instructions
  Duplicate (in pairs)
  Shuffle (within lanes)
  Permute (across lanes)
And floating-point instructions
  Subadd (subtract/add every other element)

## Slide 51: Instruction set
Number of operands addressed by the instruction set also matters
  Three is better than two (SSE vs. AVX). Why?
  Two-operand Multiply must overwrite one input operand
    What if you need to reuse that operand? You have to make a copy
    Copying increases the effective latency of the floating-point instruction

## Slide 52: Let’s be friends!
So what are the properties of complex-friendly hardware?
  Low latency (e.g. Multiply/Add instructions)
  Lots of vector registers
  Floating-point instructions with built-in swizzle
    Frees intermediate register for other purposes
    May shorten latency
  Instructions that perform complex arithmetic (ComplexMultiply/ComplexAdd)

## Slide 53: Complex-friendly hardware
Unfortunately, all of these issues must be taken into account during hardware design
Either the hardware avoids the complex “performance hazard”, or it does not
There is nothing the kernel programmer can do (except maybe befriend/bribe a hardware architect) and wait 3-5 years

## Slide 54: Summary
Complex matrix multiplication (and all level-3 BLAS-like operations) rely on a complex micro-kernel
Complex micro-kernels, like their real counterparts, must be written in assembly language to achieve high performance
The extra flops associated with complex do not make it any easier to write high-performance complex micro-kernels
Coding complex arithmetic in assembly is demonstrably more difficult than real arithmetic
  Need for careful orchestration on real/imaginary components (i.e. more difficult for humans to think about)
  Increased demand on the register set
  Need for more exotic instructions

## Slide 55: Final thought

## Slide 56: Final thought
Suppose we had a magic box. You find that when you place a real matrix micro-kernel inside, it is transformed into a complex domain kernel (of the same precision).

## Slide 57: Final thought
Suppose we had a magic box. You find that when you place a real matrix micro-kernel inside, it is transformed into a complex domain kernel (of the same precision).
The magic box rewards your efforts: This complex kernel achieves a high fraction of the performance (flops per byte) attained by your real kernel.

## Slide 58: Final thought
Suppose we had a magic box. You find that when you place a real matrix micro-kernel inside, it is transformed into a complex domain kernel (of the same precision).
The magic box rewards your efforts: This complex kernel achieves a high fraction of the performance (flops per byte) attained by your real kernel.
My question for you is: What fraction would it take for you to never write a complex kernel ever again? (That is, to simply use the magic box.)

## Slide 59: Final thought
Suppose we had a magic box. You find that when you place a real matrix micro-kernel inside, it is transformed into a complex domain kernel (of the same precision).
The magic box rewards your efforts: This complex kernel achieves a high fraction of the performance (flops per byte) attained by your real kernel.
My question for you is: What fraction would it take for you to never write a complex kernel ever again? (That is, to simply use the magic box.)
  80%?... 90%?... 100%?

## Slide 60: Final thought
Suppose we had a magic box. You find that when you place a real matrix micro-kernel inside, it is transformed into a complex domain kernel (of the same precision).
The magic box rewards your efforts: This complex kernel achieves a high fraction of the performance (flops per byte) attained by your real kernel.
My question for you is: What fraction would it take for you to never write a complex kernel ever again? (That is, to simply use the magic box.)
  80%?... 90%?... 100%?
  Remember: the magic box is effortless

## Slide 61: Final thought
Put another way, how much would you pay for a magic box if that fraction were always 100%?

## Slide 62: Final thought
Put another way, how much would you pay for a magic box if that fraction were always 100%?
What would this kind of productivity be worth to you and your developers?

## Slide 63: Final thought
Put another way, how much would you pay for a magic box if that fraction were always 100%?
What would this kind of productivity be worth to you and your developers?
Think about it!

## Slide 64: Further information
Website:
  http://github.com/flame/blis/
Discussion:
  http://groups.google.com/group/blis-devel
  http://groups.google.com/group/blis-discuss
Contact:
  field@cs.utexas.edu