## Slide 1: Implementation of Linear Algebra Libraries for Embedded Architectures Using BLIS September 28, 2015 Devangi Parikh Francisco Igual Peña Murtaza Ali

## Slide 2: Outline
TI Embedded Processors
Library Development Strategy
TI LINALG library
BLIS on C66x
Testing
Performance
Picture Credit: HP
http://processors.wiki.ti.com/index.php/MCSDK_HPC_3.x_Linear_Algebra_Library

## Slide 3: TI Embedded Processors

## Slide 4: 5 Generations of TI Multicore Processors
Keystone architecture
  Lowers development effort
  Speeds time to market
  Leverages TI’s investment
  Optimal software reuse

## Slide 5: TI 66AK2H12 SoC
Keystone II architecture
Cores
  4 ARM A15s at 1.0 GHz
    4 MB shared L2 cache
    32 Gflops single precision
    8 Gflops double precision
  8 C66x DSPs at 1.0 GHz
    32 kB L1 scratch / cache each
    1 MB L2 scratch / cache each
    128 Gflops single precision
    32 Gflops double precision
Memory
  8 GB DDR3 DRAM (external)
  6 MB shared SRAM/L3
Interfaces
  2x Gigabit Ethernet ~ 100 MB/s
  4x SRIO ~ 400 MB/s
  2x Hyperlink ~ 1 GB/s

## Slide 6: Library Development Strategy

## Slide 7: Development Philosophy
User view
  Embedded Linux running on the ARM
  Standard GCC tool chain
  Simply link to a TI provided library with an ARM callable API to accelerate applications using multiple ARM cores, DSP cores and processors as appropriate
  Use TI provided tools and examples to write new applications and libraries which use multiple ARM cores, DSP cores and processors to accelerate performance
Using multiple cores on a single processor
  OpenMP for shared memory parallelization across ARM cores
  OpenCL or OpenMP Accelerator for heterogeneous acceleration with multiple DSP cores
Using multiple processors
  Open MPI over Ethernet, SRIO or Hyperlink

## Slide 8: ARM + OpenCL DSP Acceleration

## Slide 9: TI LINALG library

## Slide 10: CBLAS
Use BLIS (BLAS-like Library Instantiation Software) for underlying BLAS computations
Advantages of using BLIS over traditional BLAS libraries
  Portable across architectures
  Generalized Matrix Storage
  Ease to use (BLAS and CBLAS compatibility layers)
  Code Reuse
Allows us to bring BLIS into embedded processing markets

## Slide 11: Single Threaded Applications
Support for the standard CBLAS and CLAPACK APIs
CBLAS runs on either the available ARM or DSP cores
Support for single core and multi core CBLAS computation
Automatically chooses between ARM and DSP cores for compute based on problem size
  User can override through environment variables
CBLAS calls to DSP are blocking

## Slide 12: Multi Threaded Applications
Application can make BLAS calls from multiple threads
ARM compute supports up to four threads (# of Application threads) x (# of CBLAS ARM compute threads) = 4
DSP compute calls are enquequed in the OpenCL command queue

## Slide 13: Compute to Data Movement Ratio
Level 3 BLAS operations are compute bound (C/D > 1)
  Automatic offloading decision available only for Level 3 BLAS operations
 | Theoretical Data Movement (D) | Compute (C) | C/D
Level 1 | 3N | N | 1/3
Level 2 | N^2+3N | 2(N^2)+N | 2N+1 / (3N+1)
Level 3 | 4(N^2) | 2(N^3) | N/2
For vector length = N, and matrix size = NxN

## Slide 14: Offload Strategy
  Automatic offloading decision available only for Level 3 BLAS operations
  Tuning : For each level 3 operation, find the matrix sizes for which the execution on DSP is faster
  Performed offline
  Sweep matrix sizes, e.g. (m,k,n) for xGEMM
  For each combination of (m,k,n), benchmark DSP execution and ARM execution
  Generate offload lookup table based on benchmarking results
Making offloading decision for each level 3 function
  Configuration through environment variable
  Offload lookup table obtained through tuning

## Slide 15: BLIS on C66x

## Slide 16: BLIS High-Performance GEMM

## Slide 17: C66x High-Performance GEMM
BLIS is designed for cache based architectures
C66x is a DMA based architecture
  Integrate DMA capabilities into BLIS to obtain high-performance on C66x
  Parallelize data movement through various levels of memory with the computation by using the DMA
Parameters are selected such that ping-pong buffers fill up the SRAM memory available
 | MC | KC | NC | MR | NR
S (single) | 144 | 428 | 944 | 4 | 8
D (double) | 132 | 220 | 864 | 4 | 4
C (single complex) | 124 | 260 | 824 | 2 | 4
Z (double complex) | 90 | 178 | 588 | 8 | 4
Parameter values for C66x

## Slide 18
Flexible
  User or library developer must be able to select when and where to transfer data for an operation
Transparent
  User must not be aware of the usage of the DMA, but if desired can manage the DMA
Integrated into the control tree mechanism
DMA Integration Goals

## Slide 19
GEMM Control Tree Definitions

## Slide 20
Memory Buffers

## Slide 21
C66x Data Movement for Level 3 BLIS
A
B
C

## Slide 22: C66x High-Performance GEMM

## Slide 23: Algorithmic Variants for GEMM

## Slide 24: Testing

## Slide 25: BLIS Test Suite
Suitable for
  Larger matrix sizes
  Performance benchmarks
  Selective functionality tests
Customizable
  Can sweep over BLAS routines with all possible permutations of the available options

## Slide 26: BLAS Test Suite
Suitable for
  Corner cases (zero matrix dimension, near-underflow and near-overflow valued matrices)
  Smaller matrix sizes
Not customizable
Total tests = 239,052

## Slide 27: CLAPACK Test Suite
Suitable for
  Corner cases (zero matrix dimension, near-underflow and near-overflow valued matrices)
  Smaller matrix sizes
Not customizable
Types of tests = 83
Total tests = 3,073,466

## Slide 28: Performance

## Slide 29: SGEMM
Single precision general matrix-matrix multiplication
Obtained using a TI 66AK2H12 SoC at a 1 GHz clock
Theoretical peak DSP performance = 128 GFLOPS
Theoretical peak ARM performance = 32 GFLOPS

## Slide 30: DGEMM
Double precision general matrix-matrix multiplication
Obtained using a TI 66AK2H12 SoC at a 1 GHz clock
Theoretical peak DSP performance = 32 GFLOPS
Theoretical peak ARM performance = 8 GFLOPS

## Slide 31: Thanks!