## Slide 1: Formal Verification in the Industry: a 2020 Vision VIGYAN SINGHAL Oski Technology

## Slide 2: My Formal Journey
University Researcher
(4 years 1991-1995)
(UC Berkeley)
Goal: advance state-of-the-art
EDA tool developer
(10 years 1995-2005)
(Jasper, Cadence)
Goal: build competitive tools
Semiconductor tool user
(10 years 2005-2015)
(Oski)
Goal: optimize time-to-market and cost

## Slide 3: Hardware Design is Hard
Hard to Design
  Programmer LOC productivity is > 10X lower than software design
    Massively parallel program (each always block is a thread!)
  Have to worry about not just functionality
    Low-level performance – within one clock cycle!
    Power
    Area on silicon
    No higher-level abstraction – e.g. synchronization, OO
  Most designers are great craftsmen, not great mathematicians
Hard to Verify

## Slide 4: Hard to Verify – Example Schedule
post-si
WARs
subsystem fixes + minor features
uarch
reqs
RTL
coding
sandbox
verif.
bugs + timing
fixes
ECO
fixes
post-ECO
WARs
12-month schedule

## Slide 5: Current Design & Verification Challenges
Implicit wall between design and verification engineers
  Infrequent communication
  Miscommunication
  Delay in communication
Drawback
  Loss of efficiency and productivity
  Lack of design quality
  Prolonged project cycle
    Verification is taking too long
  Missing bugs after tapeout

## Slide 6: Ziyad Hanna: “Typical Design & Validation Work Flows - two “disconnected” tasks”
Validation
Design
Arch and uArch exploration
RTL Rev 1
RTL Freeze
>95% Quality
CKT Design
Parallel Design
RTL Rev0
Coding Done
Black Box
Unit/FC Test Plan
Validation
Data Base
Unit Level Val
Full Chip Val
System Val
Emulation
Env/Flow Dev
Validation
Flows
Simulation,
Coverage,
FPV,
Emulation
Parallel Validation
Arch Val.
Spec Dev.
Notes: Two parallel tracks
Designers focus on RTL implementation to meet timing, power and area targets
Verification engineers focus on black-box verification. They understand the spec but do not understand the implementation
There is are disconnected activities and therefore the huge risk on quality, productivity and schedule

## Slide 7: My 2020 Vision

## Slide 8: Taking Insight from Pair Programming
Pair programming
  Agile software development technique: two programmers develop software side by side at one computer
  The driver writes code
  The observer reviews each line of code as it is typed in
  The two programmers switch roles
Pair programming benefits
  Improve design quality
  Reduce defects
  Reduce staffing risk
  Enhance technical skills
  Improve team communications
  Considered more enjoyable than traditional practice

## Slide 9: Paired Formal Design
Each designer is paired with a formal verification engineer
  Microarchitecture decisions take formal plan into consideration
  Formal engineer gains intimate knowledge of design
    A must have for formal engineers to apply techniques likes abstraction
  Designer can have another pair of eyes to check implementation
  Designer can bravely try optimizations, timing and power fixes
  Unlike Pair Programming, roles are not inter-changeable
Paired Formal Design benefits:
  Improve design quality
  Reduce project cycle & cost
    Verification is done when design is done
  Late-stage fixes take 10X less time
  Each can fix bugs!
Organizational hierarchy?
Seat assignment?
Hiring?

## Slide 10: Improved Schedule and Quality at No Extra Cost
post-si
WARs
subsystem fixes + minor features
uarch
reqs
RTL
coding
sandbox
verif.
bugs + timing
fixes
ECO
fixes
post-ECO
WARs
minor
features
uarch
reqs
RTL coding +
formal verification
timing
fixes
ECO
fixes
2X savings in schedule
no increase in resources
12-month schedule

## Slide 11: What Kind of Formal Tools
Outstanding UX
Ability to specify abstractions, symmetry, proof decompositions
Guides when problem is intractable
Links to coverage and completeness
…