## Slide 1: Routing under Constraints
Alexander Nadel Intel, Israel
FMCAD
Mountain View CA, USA
October 4, 2016

## Slide 2
"PhysicalDesign" by Linear77 - Own work. Licensed under CC BY 3.0 via
Wikimedia Commons - https://commons.wikimedia.org/wiki/File:PhysicalDesign.png#/media/File:PhysicalDesign.png
Routing

## Slide 3: Outline
Goal: Design a Scalable Design Rule-aware Router
Routing under Constraints (RUC): Problem Formalization
Bit-Vector / SAT Encoding
DRouter through SAT Solver Surgery
Doesn’t scale
A*-based decision strategy (emulates constraints!)
Net restarting & net swapping
Graph conflict analysis
Unsolved crafted and industrial RUC instances are routed!

## Slide 4
Abboud et al, OR Spectrum’08

## Slide 5: Routing: Input (AKA Steiner Tree Packing Problem)
Input
A graph G(V,E)
Disjoint Nets Ni  V
Terminals

## Slide 6: Routing: Output
Input
Output
Each net is spanned by a tree, called the net routing
Net routings can’t intersect
Optimization: minimize the total routing length
It is NP-hard to find:
Shortest solution for one multi-terminal net (Steiner tree problem)
Any solution for many multi-terminal nets

## Slide 7: Design Rules
Routing is to satisfy design rules
  Originating in the manufacturing requirement
Example “short” rule:
  The 2 vertices of any edge can’t belong to two distinct net routings
Short rule is violated for these edges
When the short rule is on, this example is UNSAT

## Slide 8: Industrial Approach: Rip-Up and Reroute
Nets are routed one-by-one
  Using A*
    s-t shortest-path given costs’ under-approximation
    A*Dijkstra if no costs’ under-approximation is provided
  Trying to heuristically obey design rules
Violations are allowed, hence the initial solution might be problematic
  Net routings might intersect
  Design rules might be violated
Clean-up is applied
  Rip-up: problematic net routings are removed
  Reroute: un-routed nets are attempted again

## Slide 9: The Problem with the Current Solution
Design rule violations persist
  Manual clean-up is carried out
Some violations still persist
Time-to-market is impacted

## Slide 10: Potential Solution
Constraint Solving
Next: formalizing Routing under Constraints

## Slide 11: Routing Induces Assignment
Edge variables
Bool e: edge activity

## Slide 13
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
1
1
1
0
0
1
1
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
1
1
1
1
1
1
1
1
1
1
1
0
0
0
0
0
0
1
1
1
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0

## Slide 14: Routing Induces Assignment
Bool v: activity status
Bit-vector n: net id
( for inactive vertices)
Vertex variables

## Slide 16
0,
0,
0,
0,
0,
1,1
0,
0,
0,
0,
0,
0,
0,
0,
0,
1,1
0,
0,
0,
0,
0,
0,
0,
0,
0,
1,1
0,
0,
0,
0,
0,
0,
0,
0,
0,
1,1
0,
0,
0,
0,
0,
0,
0,
0,
0,
1,1
0,
0,
0,
0,
1,0
1,0
1,0
1,0
1,0
1,1
1,0
1,0
1,0
1,0
0,
0,
0,
0,
1,0
1,1
1,0
0,
0,
0,
0,
0,
0,
0,
1,0
1,1
1,0
0,
0,
0,
0,
0,
0,
0,
1,0
1,1
1,0
0,
0,
0,
0,
0,
0,
0,
1,0
1,0
1,0
0,
0,
0,

## Slide 17: Modeling Routing under Constraints
Design rules can be easily expressed in BV logic
  Variables:
    Edge & vertex activities
    Vertex nids
    Any auxiliary variables
“Short” rule example
  For every edge e=(v,u): v  u  nid(v)=nid(u)
Short rule is violated for these edges

## Slide 18: Routing under Constraints (RUC): Problem Formulation
Graph G(V,E)
Disjoint Nets Ni  V
Input
A quantifier-free bit-vector formula F(V  E  N  A)
  V : vertex activity
  E : edge activity
  N : vertex net id
  A : any auxiliary variables
(represents the design rules)
Output: a model to F, which induces a routing:
e=(v,u) is active 
  v and u are active, and
  nid(v) = nid(u)
For each net i: active vertices with nid i and active edges span the net’s terminals
Optional optimization requirement: the overall weight of active edges is as small as possible

## Slide 19: Solving Attempt: Encoding into Bitvector Logic / SAT
For 2-terminal nets:
  e=(v,u) is active 
    v and u are active, and
    nid(v) = nid(u)
  A terminal has one active neighbor edge
  An active non-terminal has two active neighbor edges
For n-terminal nets:
  Encode directed trees
    Using edge directions

## Slide 20: SAT Solver’s Internals
Decision Strategy
(Conflict-driven)
Boolean Constraint
Propagation
Conflict Analysis &
Learning
Backtracking
Restarts
Time-to-restart?
No conflict
Conflict

## Slide 21: SAT  DRouter through Surgery

## Slide 22
Decision Strategy
(Conflict-driven)
Boolean Constraint
Propagation
Conflict Analysis &
Learning
Backtracking
Restarts
Time-to-restart?
No conflict
Conflict
A*-based Router
Graph-based
Learning
Net
Swapping
Net
Restarting
Time-to-flip?
Time-to-
restart?
SAT  DRouter

## Slide 23: DRouter
Decision Strategy
(Conflict-driven)
Boolean Constraint
Propagation
Conflict Analysis &
Learning
Backtracking
No conflict
Conflict
A*-based Router
Graph-based
Learning
Net
Swapping
Net
Restarting
Time-to-flip?
Time-to-
restart?
Encoded constraints:
Edge consistency
  e=(v,u) is active 
    v and u are active
    nid(v) = nid(u)
User-provided constraints modelling design rules
That’s it! What about disconnected terminals???
Routing correctness is guaranteed by the decision strategy!

## Slide 24: 1-Net Example
Decision Strategy
(Conflict-driven)
Boolean Constraint
Propagation
Conflict Analysis &
Learning
Backtracking
No conflict
Conflict
A*-based Router
Graph-based
Learning
Net
Swapping
Net
Restarting
Time-to-flip?
Time-to-
restart?

## Slide 25: 1-Net Example
0
1
2
1
2
3
s: (0, 0)
t: (3, 0)
¬(1,0)  ¬(2,0)
¬(1,0)  ¬(1,1)
¬(3,2)  ¬(3,1)
Initial path:
A* from s->t
Real path
x
x
σ (sugg.)
σ-violation
Activate edge in sugg.
  A* search
  for new σ
SAT
Decision
Path Suggestion
(not an actual SAT decision)
Design rules

## Slide 26: 1-Net Example
0
1
2
1
2
3
s: (0, 0)
t: (3, 0)
¬(1,0)  ¬(2,0)
¬(1,0)  ¬(1,1)
¬(3,2)  ¬(3,1)
Initial path:
A* from s->t
Real path
x
x
σ (sugg.)
  A* search
  for new σ
No -violation
Path found
Target is part of path?
no
Repeat
Activate edge in sugg.
BCP

## Slide 27: 1-Net Example
0
1
2
1
2
3
s: (0, 0)
t: (3, 0)
¬(1,0)  ¬(2,0)
¬(1,0)  ¬(1,1)
¬(3,2)  ¬(3,1)
Initial path:
A* from s->t
Real path
x
x
σ (sugg.)
  A* search
  for new σ
Activate edge in sugg.
x
σ-violation
No -violation
Target is part of path?
no
Repeat

## Slide 28: 1-Net Example
0
1
2
1
2
3
s: (0, 0)
t: (3, 0)
¬(1,0)  ¬(2,0)
¬(1,0)  ¬(1,1)
¬(3,2)  ¬(3,1)
Initial path:
A* from s->t
Real path
x
x
σ (sugg.)
  A* search
  for new σ
Activate edge in sugg.
x
σ-violation
Add conflicting clause: vertex cut (2,0)  (3,1)
1UIP conflict clause: (2,0)  ¬(3,2)
(2,0)  ¬(3,2)
x
Graph conflict (s and t can’t be connected)
  Learn & Backtrack
No -violation
Target is part of path?
no
Repeat

## Slide 29: 1-Net Example
0
1
2
1
2
3
s: (0, 0)
t: (3, 0)
¬(1,0)  ¬(2,0)
¬(1,0)  ¬(1,1)
¬(3,2)  ¬(3,1)
Initial path:
A* from s->t
Real path
x
x
σ (sugg.)
  A* search
  for new σ
No σ-violation
Path found
Graph conflict
  Learn & Backtrack
DONE!
Target is part of path?
(yes!)
no
Repeat
Activate edge in sugg.
x
Result:
Path that follows constraints!
(2,0)  ¬(3,2)
σ-violation

## Slide 30: Multiple Nets Handling
Route the nets one-by-one
  Order is critical!
Example Order 1:
  Violet
  Black
  Red
Example Order 2:
  Red
  Black
  Violet

## Slide 31: Multiple Nets Handling
Route the nets one-by-one
  Order is critical!
Example Order 1:
  Violet
  Black
  Red
Example Order 2:
  Red
  Black
  Violet
Too slow! Solution: dynamic net reordering!
Graph conflict
  black is blocked
Early conflict detection
  Check for graph conflicts after routing each terminal
Learn a conflict clause &
re-route

## Slide 32: DRouter
Decision Strategy
(Conflict-driven)
Boolean Constraint
Propagation
Conflict Analysis &
Learning
Backtracking
No conflict
Conflict
A*-based Router
Graph-based
Learning
Net
Swapping
Net
Restarting
Time-to-flip?
Time-to-
restart?

## Slide 33: Net Swapping
Example Order 2:
  Red
  Black
  Violet
Flip:
  Black
  Red
  Violet
Swapped
Net Swapping:
  After N conflicts, swap the order between:
    the first blocked net i
    the blocking net j
  {A,j,B,i,C}  {A,i,j,B,C}

## Slide 34: Net Restarting
Example Order 2:
  Red
  Black
  Violet
Flip:
  Black
  Red
  Violet
Moved to the top
Net Restarting
  Restart and move the blocked net to the top
    (after M conflicts for that net)

## Slide 35: Net Swapping vs. Net Restarting
Swapping is local
Restarting is global
In practice both techniques are crucial
Strategy:
  Swap for some time
  If it doesn’t work, restart

## Slide 36: Related Work 1: Clock Routing Erez & Nadel, CAV’15
Reduction to finding bounded-path in graph
SAT solver surgery: graph-aware decision strategy & graph conflict analysis
The decision strategy:
  Emulates constraints!
  Guides the solver towards the solution
  Considers additional optimization requirements
Clock Routing

## Slide 37: Related Work 2: Monosat Solver Bayless & Bayless & Hoos & Hu, AAAI’15
Can reason about graph predicates & SAT/BV
Graph conflict analysis
Shortest-path decision heuristic can be optionally applied
Path-finding (routing for one 2-terminal net) is conceptually similar in Monosat and DRouter
  Main difference:
    Lazy A* in DRouter vs.
    Eager incremental Ramalingam-Reps in Monosat
RUC can be easily expressed in Monosat language

## Slide 38: Monosat vs. DRouter for Routing under Constraints
Monosat’s algorithms are not routing-aware
  No net re-ordering
  Graph conflict analysis for routing is inefficient
Routing in DRouter (net swapping&restarting are off)
Routing in Monosat
Conflict
Conflict

## Slide 39: Experimental Results on Crafted Instances
Solvers:
  Drouter (default)
  Drouter – R: no net restarting
  Drouter – S: no net swapping
  Drouter – SR: no net swapping, no net restarting
  Monosat (default)
  Monosat + D: shortest-path decision strategy is on
  BV: reduction to BV
Instances:
  120 solid grid graphs of size M  20
    M  {3,5,7}
  20 random 2-terminal nets
  Generate C * |V| random binary clauses v  u
    v,u  V
    C  {0,0.1,0.2,0.3}

## Slide 40
Chart: C: Clause%
| 0 | 10 | 20 | 30
DRouter | 30 | 30 | 30 | 30
Drouter-R | 0 | 10 | 0 | 10
DRouter-S | 30 | 10 | 10 | 10
DRouter-SR | 0 | 0 | 0 | 0
Monosat | 0 | 0 | 0 | 0
Monosat+D | 0 | 0 | 0 | 0
BV | 0 | 0 | 0 | 0
Full-fledged DRouter only can solves all the instances
  Both net restarting and net swapping are essential!
Monosat and BV can’t solve a single instance

## Slide 41: DRouter on Industrial Instances
Run DRouter on difficult clips from Intel designs
  Couldn’t be routed cleanly by 2 industrial routers
Area in m2 | Nets | Vertices | Constraints | Time in sec. | Memory in Gb.
24 | 110 | 42,456 | 484,008 | 25 | 0.7
24 | 230 | 42,456 | 484,008 | 391 | 1.0
32 | 352 | 63,740 | 667,764 | 705 | 2.2
129 | 788 | 127,480 | 2,669,056 | 14,733 | 6.5
129 | 891 | 127,480 | 2,669,056 | 92,950 | 6.5

## Slide 42: Conclusion
DRouter: design-rule-aware router
  SAT solver surgery:
    Decision heuristic  A*-based router
    Conflict analysis enhanced with graph reasoning
    Restarts  net swapping & net restarting
Solves instances which can’t be solved by existing tools
  Including clips from real Intel designs