## Slide 1: Testing Composable Specifications
Ken McMillan
Microsoft Research

## Slide 2: Case study
TileLink is a protocol for implementing a coherent memory in a system-on-chip (SoC).
Goal: a formal, modular specification of TileLink
  Specify the protocol
  Prove that it implements correct memory semantics
  Rigorously test component implementations
  Allow rapid configuration of SoC designs

## Slide 3: TileLink system
Hierarchy of memory system components for SoC using a common interface protocol.
CORE
CORE
CORE
L2$
NET
DIR
DIR
MEM
MEM
L2$
DIR
MEM
TL
TL
TL
TL
Hierarchy implements weakly consistent memory model.

## Slide 4: Modular verification
General approach:
  Write generic formal specifications of components
  Verify components locally against specifications
  Infer that systems of such components are correct
Composable specifications:
  Correctness of components implies correctness of system.
  With a composable specification, we can assemble arbitrary configurations of components.
Some composable specifications are better than others, however…

## Slide 5: Good composability
Assume/guarantee specifications
  A conjunction of temporal properties of interfaces
  Assume/guarantee relationships
A
B
A: “”
B: “”
AB: “”
composable!
This proof is checkable in P-time
We want our specifications to be composable “by construction”.

## Slide 6: Memory semantics
Memory operations:
op(loc,kind,addr,data)
CPU
read
write
atomic
Happens-before relation on operations:
happens-before() loc() loc() time() < time()
Weak consistency:
A set of operations is weakly consistent if there exists an ordering s.t:
  respects happens-before
  is consistent
Consistency:
A sequence of ops is consistency if every read sees value of most recent write.
(addr() addr() atomic() atomic())

## Slide 7: Problem
How do you write a “good” composable specification for a system if its key property refers to all events in the system?
How do we witness the serialization ?
How do local operations fit into the global serialization?

## Slide 8: Solution
Add a “reference object”.
  Constructs the witness for .
  Verifies consistency as it is constructed
These operations allow us to define the semantics of the system interfaces.
ref.
create
commit
create : op loc stamp
commit : stamp unit
eval : stamp value
eval
mem
commit(stamp):
assumes happens-before(X,op(stamp)) committed(X)
value = eval(stamp):
guarantees value = result(,op(stamp))
assumes committed(stamp)

## Slide 9: TileLink system
Hierarchy of memory system components for SoC using a common interface protocol.
CORE
CORE
CORE
L2$
NET
DIR
DIR
MEM
MEM
L2$
DIR
MEM
TL
TL
TL
TL

## Slide 10: TileLink interface protocol
Protocol messages implement
  Coherent requests (MESI)
  Invalidation
  Ordered, non-coherent operations
Interface has two roles:
  Client processor
  Manager memory
Acquire
Grants
Finish
Probe
Release
client
manager
Typical transaction flow at interface

## Slide 11: Writing a “good” composable spec
Specification has two parts:
  Temporal properties of interface
  Assume/guarantee relationships between properties
Interface properties of two types:
  Interface protocol properties
  Semantic properties, relative to reference object

## Slide 12: Semantic interface properties
Manager-side properties
  M[1]: Data in cached Grant must match ref.mem.
  M[2]: If uncached resp. then committed(stamp)
  M[3]: If uncached resp. then data = eval(stamp)
Client-side properties
  C[1]: Data in cached Release must match ref.mem.
  C[2]: If uncached req. then happens-before(X,stamp) implies requested(X).
  C[3]: If uncached resp. then data = eval(stamp)
These properties refer to the reference object to define ordering and data values at the interface.

## Slide 13: Commitment properties
Client-side commitments:
  SC[1]: Read may be committed on client side only if interface has shared or exclusive permissions.
  SC[2]: Write may be committed on client side only if interface has exclusive permissions.
Manager-side properties
  SM[1]: Read may be committed on manager side only if interface has shared or invalid permissions.
  SM[2]: Write may be committed on manager side only if interface has invalid permissions.
The coherence state determines what commitments are allowed on either side of the interface. This is the function of coherence.
Note: “client side” means any component left of the interface.

## Slide 14: Assume/guarantee relationships
An L2 cache has TileLink interfaces on processor side and memory side.
reference object
…
…

## Slide 15: Assume/guarantee relationships
An L2 cache has TileLink interfaces on processor side and memory side.
reference object
…
…
P,R:
P,R:
P,R:
P,R:
Checking this proof is a purely syntactic operation

## Slide 16: Formal proofs
We can now formally verify components in isolation against their assume/guarantee specifications:
  Reording buffer
  Hierarchical cache
  Processor, memory, etc.
These are simple abstract component models, intended to show that the specification has the intended implementations.
  Show key property that protocol is insensitive to message re-ordering.
  In the process, specification was corrected.
Because our assume/guarantee specification is composable, we know that hierarchies built from these components implement a weakly consistent shared memory.

## Slide 17: Compositional testing
From an assume/guarantee specification, we can automatically generate a test environment.
reference object
RTL
…
…
generate
generate
check
check
Tested two RTL level components with randomized generation using Z3:
  L2 cache bank
  Snooping hub
check

## Slide 18: Testing results
Compositional testing revealed currency errors in the RTL in under 1s (< 100 cycles)
  Unit testing provides much greater flexibility in covering internal corner cases
  Randomized specification-based testing reduces bias
Latent bugs
  Most bugs could not be stimulated in integration test
  Latent bugs affect re-usability
Importance of composability
  All system-level errors exposed to unit testing
  Gain confidence that components can be assembled into arbitrary configuration.

## Slide 19: Conclusion
Good composable specification is such that:
  Correct component imply correct system
  The proof of this is efficiently checkable
Global properties (such as memory consistency)
  Reference object + temporal assume/guarantee
  Allows local specification of interface semantics
Composable TileLink interface spec provides:
  Documentation of the interface
  Ability to reason formally about specification
  Efficient and rigorous test to find latent bugs
Composable specifications provide a way to formal verification experts to provide value in an environment where most engineers do not have formal skills.

## Slide 20: Specification as a social process
The specification develops over time in collaboration with the system architects.
  Ambiguities in informal specs must be resolved.
  Initial formal spec almost certainly does not reflect designers intention.
  Mismatch with implementation may indicate properties should be strengthened or weakened for efficiency.
Over time the formal spec becomes a valuable document.
  Encapsulates design knowledge.
  Allows rigorous testing and verification.