## Slide 1: Formal Verification of Hardware Support For Advanced Encryption Standard
Anna Slobodová
Centaur Technology
This work was done while at Intel

## Slide 2: Outline of the talk
AES algorithm and instructions
  sketch of the algorithm
  mapping to AES instructions
  operations over GF
Verification of AES instructions
  Verification framework
  BDD variable ordering that works

## Slide 3: AES algorithm and instructions
Cipher(byte in[16], byte out[16], word w[4*(Nr+1)])
begin
  byte state[4, 4]
  state = in
  AddRoundKey(state, w[0,3]
  for round = 1 step 1 to Nr-1
    SubBytes(state)
    ShiftRows(state)
    MixColumns(state)
    AddRoundKey(state, w[4*round, 3*(round+1)]
  end for
  SubBytes(state)
  ShiftRows(state)
  AddRoundKey(state, w[4*Nr,3*Nr+1]
  out = state
end
AESENC
AESENCLAST
AESDEC, AESDECLAST, AESKEYGENASSIST, AESIMC
Notes: Rijndael algorithm is a symmetric block cipher that can
process data blocks of 128 bits, using cipher keys with lengths of 128, 192, and 256 bits.
Here is a pseudo-code taken from FIPS 197 for AES-128 encryption. Intel’s microprocessors support the algorithm through
Instructions AESENC that comprises to one round of the algorithm, and AESENCLAST that corresponds to the last round.
Symmetrically, we have a decryption algorithm and associated instructions AESDEC and AESDECLAST.
Last two instructions are used to generate and manipulate keys.

## Slide 4: AES bytes, words and state
Byte - basic unit, 8 bits
  - Interpreted as polynomials
State – array of bytes
word ≈column
[w0 w1 w2 w3]

## Slide 5: Galois Field 28
elements = bytes
  7th degree polynomials with binary coefficients
addition = subtraction = bit-wise XOR
multiplication = multiplication of polynomials modulo irreducible polynomial

## Slide 6: Polynomials with coefficients in GF(28)
words = 4th degree polynomials with coefficients in GF(28)
addition = addition in GF(28) of corresponding bytes
(modular) multiplication = multiplication of polynomials modulo polynomial x4+1

## Slide 7: ShiftRows

## Slide 8: S-box transformation
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | A | B | C | D | E | F
0 | 63 | 7c | 77 | 7b | f2 | 6b | 6f | c5 | 30 | 01 | 67 | 2b | fe | d7 | ab | 76
1 | ca | 82 | c9 | 7d | fa | 59 | 47 | f0 | ad | d4 | a2 | af | 9c | a4 | 72 | c0
2 | b7 | fd | 93 | 26 | 36 | 3f | f7 | cc | 34 | a5 | e5 | f1 | 71 | d8 | 31 | 15
3 | 04 | c7 | 23 | c3 | 18 | 96 | 05 | 9a | 07 | 12 | 80 | e2 | eb | 27 | b2 | 75
4 | 09 | 83 | 2c | 1a | 1b | 6e | 5a | a0 | 52 | 3b | d6 | b3 | 29 | e3 | 2f | 84
5 | 53 | d1 | 00 | ed | 20 | fc | b1 | 5b | 6a | cb | be | 39 | 4a | 4c | 58 | cf
6 | d0 | ef | aa | fb | 43 | 4d | 33 | 85 | 45 | f9 | 02 | 7f | 50 | 3c | 9f | a8
7 | 51 | a3 | 40 | 8f | 92 | 9d | 38 | f5 | bc | b6 | da | 21 | 10 | ff | f3 | d2
8 | cd | 0c | 13 | ec | 5f | 97 | 44 | 17 | c4 | a7 | 7e | 3d | 64 | 5d | 19 | 73
9 | 60 | 81 | 4f | dc | 22 | 2a | 90 | 88 | 46 | ee | b8 | 14 | de | 5e | 0b | db
a | e0 | 32 | 3a | 0a | 49 | 06 | 24 | 5c | c2 | d3 | ac | 62 | 91 | 95 | e4 | 79
b | e7 | c8 | 37 | 6d | 8d | d5 | 4e | a9 | 6c | 56 | f4 | ea | 65 | 7a | ae | 08
c | ba | 78 | 25 | 2e | 1c | a6 | b4 | c6 | e8 | dd | 74 | 1f | 4b | bd | 8b | 8a
d | 70 | 3e | b5 | 66 | 48 | 03 | f6 | 0e | 61 | 35 | 57 | b9 | 86 | c1 | 1d | 9e
e | e1 | f8 | 98 | 11 | 69 | 8d | 8e | 94 | 9b | 1e | 87 | e9 | ce | 55 | 28 | df
f | 8c | a1 | 89 | 0d | bf | e6 | 42 | 68 | 41 | 99 | 2d | 0f | b0 | 54 | bb | 16
Notes: S-box transformation, also called Sub-transformation is an application of a non-linear transformation on each byte of the state.
It is computed as a composition of multiplicative inversion of the elements in GF(28) and an affine transformation over GF(2). It can be represented by a table called S-box.

## Slide 9: MixColumns
Notes: MixColumns is a transformation of state where each column is replaced with a transformed column. The transformation is defined as multiplication of polynomials with coeficients in GF(28) module polynomial x4+1. Such multiplication is called modular multiplication to distinguish it from the multiplication in GF(28). For each column, we apply modular multiplication to a special polynomial q and the column. This is the same as a left-side multiplication of the matrix M(q) to the column.

## Slide 10: Verification of AES instructions
Data-path proof
Control proof
AES
Symbolic inputs
Symbolic outputs
Symbolic inputs
Symbolic outputs
weakening
weakening
e0 e1 e2
X X d2
X X 0
X X e2
0 0 1
d2

## Slide 11: BDD variable ordering for AES instructions

## Slide 12: Conclusions
Hardware support for AES instructions can be done using BDD based simulation engine.
There is a common BDD variable ordering that can be used across all symbolic simulation runs.