## Slide 1: Post-silicon Timing Diagnosis Made Simple using Formal Technology
Daher Kaiss, Jonathan Kalechstain
Formal Engines and Technologies Team
Core CAD Technologies
Intel Corp. - Haifa

## Slide 2: Agenda
Motivation
Speed path debug at Intel
Introducing our tool: NGSPA
  Next Generation Speed Path Analyzer
Results
Challenges and next steps

## Slide 3: Static Timing Analysis
An important pre-silicon design activity
Pros: Aims to compute the expected timing to a digital circuit without requiring simulation
Cons: miscorrelation between the pre. and post silicon behaviors
  usage of simplified delay models:
  limited ability to consider the effects of logical interactions between signals
Result: about 5% of the chip frequency is achieved by post silicon speed path debug

## Slide 4: Post-silicon Speed Debug
Time consuming process
  Hundreds of speed paths for some chips
Based on Laser Assisted Device Alternation (LADA)
  Costly machines (>$1 Million per machine)
  Requires skilled operators
  Serial process
  Some units might be burnt/broken
TTM requirements sometimes cause projects to go with low GHz

## Slide 5: How it was done so far
Reproduce the Failure
Isolate and Id Speedpath
Probing
Failures to Debug
“ZBB”ed Failures
Debug Each Failure
Collect All Failures
Validation
Si. Debug
Bug Fix

## Slide 6: Timing Domains
A timing domain is a set of HW devices controlled by a common clock
Combinatorial
Block
Combinatorial
Block
Combinatorial
Block
SRC clock domain
DST clock domain
Optical Probing

## Slide 7: What is NGSPA?
Next Generation Speed Path Analyzer
A new CAD tool for preforming speed path isolation
Enables replacing >$1M optical probing (LADA) machines with CAD application running on a $1K x86 server
Saving machine cost
Saving machine operators resource
From serial LADA execution  Parallelized CAD
From burnt/broken units  Deterministic SW
Optical Probing
NGSPA

## Slide 8: Inputs to NGSPA
Gate level schematic model (Structural Verilog)
A trace produced by simulating a trace on the RTL
  Either RTL simulation (~overnight)
  Or, Emulation trace (~2 hours)
Failing scan and failing cycle
Path length
  10-20 cycles
Source and Destination timing domains

## Slide 9: How it works
CORE
Block1
SRC
Block2
Block3
Block4
DST
Block5
Block6
CORE
A
B
Failing Scanout
SRC Domain
DST Doamin

## Slide 10: A speed path
Scan
Inputs
SRC
domain
DST
domain
Not widely inserted

## Slide 11: Our approach for isolating speed paths
Reproduce the functional behavior of the speed path
  Instead of silicon debug, we use the logical model of the design
Assumptions:
  The speed path was triggered by a logic transition at one of the sequentials in the source domain

## Slide 12: Using SAT for Backward propagation
1
0
X
0
1
0
1

X
1

X
1

X
0


## Slide 13: Finding Speed paths
Scan
Scan
SRC
SRC
SRC
Inp1
[v0,v1,…, vj, .. vk]
Stimuli from Trace
[?,?,…, NOT vj, .. ?]
Flipping Scanat scanout_phase(=j)
Only one selector is high
Same inputs with same values
Same free inputs
Inp2
Scan
Scan
Scan
DST
DST
Scan
SRC
SRC
SRC
Inp1
Inp2
Scan
Scan
Scan
DST
DST
Scan

## Slide 14: First Challenge: Reconverging logic
A
Out [F]
[F]
[F]
[T]

## Slide 15: In a more general way
SRC
Scan
f

## Slide 16: Handling Reconverging Paths
Scan
f
Scan
f
SRC
SEL-1
SEL-2
SEL-3
Mutex (SEL-2, SEL-3)

## Slide 17: Second Challenge: Dealing with complexity
Block1
SRC
Block2
Block3
Block4
DST
Block5
Block6
CORE
A
B

## Slide 18: Iterative Cone Expansion

## Slide 19: Iterative Cone Expansion
j-4
j-3
j-2
j-1
j
j
j
Failing Scan
j

## Slide 20: Results
Test No. | # signals in cone | # of inputs on oundary | # of latches in cone | # of econverg. signals | # of iterations | path length (in phases) | # of paths | Run Time (Sec.)
1 | 296 | 26 | 2 | 4 | 5 | 3 | 1 | 248
2 | 509 | 67 | 14 | 11 | 6 | 4 | 1 | 278
3 | 405 | 54 | 3 | 12 | 11 | 8 | 1 | 214
4 | 305 | 19 | 3 | 0 | 6 | 4 | 1 | 290
5 | 248 | 11 | 1 | 0 | 1 | 1 | 1 | 186
6 | 517 | 50 | 14 | 26 | 55 | 44 | 1 | 227
7 | 497 | 83 | 4 | 3 | 7 | 4 | 1 | 222
8 | 1528 | 212 | 59 | 86 | 14 | 8 | 1 | 745
9 | 27696 | 3009 | 635 | 8569 | 31 | 16 | 1 | 7168
10 | 3025 | 617 | 43 | 650 | 15 | 8 | 2 | 434
11 | 2403 | 345 | 22 | 209 | 12 | 7 | 2 | 318
12 | 1798 | 258 | 58 | 236 | 33 | 20 | 2 | 442
13 | 855 | 164 | 8 | 27 | 8 | 5 | 3 | 222
14 | 25895 | 7279 | 294 | 1070 | 30 | 16 | 3 | 6458
15 | 21864 | 4618 | 165 | 2266 | 33 | 18 | 3 | 3395
16 | 855 | 164 | 8 | 27 | 8 | 5 | 4 | 242
17 | 1545 | 303 | 46 | 5 | 12 | 6 | 5 | 5555
18 | 837 | 90 | 39 | 29 | 23 | 12 | 6 | 619
19 | 4665 | 704 | 106 | 1149 | 31 | 18 | 7 | 579
20 | 8789 | 994 | 125 | 2132 | 26 | 14 | 7 | 1713
21 | 26226 | 4035 | 168 | 2422 | 27 | 14 | 15 | 3285
22 | 4931 | 675 | 167 | 689 | 27 | 14 | 40 | 780

## Slide 21: How speed paths looks like
SRC
DST
SRC
DST
SRC
SRC
DST
SRC
S
B
A

## Slide 22: Results
Chart: 
| A0 | B0 | P0 | C0
Steppintg | 0 | 0 | 0 | 0
NGSPA | 2 | 4 | 18 | 22
LADA | 19 | 0 | 1 | 2
Day per speed path | 2.0952 | 2.75 | 1.5263 | 0.75

## Slide 23: Progress so far
>90% of the optical probing activity was saved
One of two LADA machines in the debug lab will be released
Work on progress deployment this technology across Intel
Limitations:
  No failing scan was detected, despite the fact that the test failed

## Slide 24: Future work
Can we drop the need for RTL simulation/emulation and use scan dump traces only?
  Pros: faster TAT
  Cons: less observability
Use same technology for yield analysis

## Slide 25: Summary
NGSPA is one of the great examples demonstrating the glory of formal verification
  Ability to replace laser based machines with CAD
Same technology can be applied to other adjacent areas like : fault isolation & glitch detection
Formal technologies (SAT and SMT) are being deployed in other interesting areas in Intel
  Tester scheduling, layout routing and filling and others

## Slide 26
Thank You