## Slide 1: Microarchitectural Performance Characterization of Irregular GPU Kernels
Molly A. O’Neil and Martin Burtscher
Department of Computer Science

## Slide 2: Introduction
GPUs as general-purpose accelerators
  Ubiquitous in high performance computing
  Spreading in PCs and mobile devices
  Performance and energy efficiency benefits…
…when code is well-suited!
  Regular (input independent) vs. irregular (input determines control flow and memory accesses)
  Lots of important irregular algorithms
    More difficult to parallelize, map less intuitively to GPUs

## Slide 3: Outline
Impact on GPU performance characteristics of…
  Branch divergence
  Memory coalescing
  Cache and memory latency
  Cache and memory bandwidth
  Cache size
First, review GPU coding best practices for good performance

## Slide 4: Best Practice #1: No Divergence
To execute in parallel, threads in a warp must share identical control flow
  If not, execution serialized into smaller groups of threads that do share control flow path  branch divergence

## Slide 5: Best Practice #2: Coalescing
Memory accesses within a warp must be coalesced
  Within a warp, memory references must fall within the same cache line
  If not, accesses to additional lines are serialized

## Slide 6: Best Practice #3: Load Balance
Balance work between warps, threads, and thread blocks
All 3 difficult for irregular codes
  Data-dependent behavior makes it difficult to assign works to threads to achieve coalescing, identical control flow, load balance
Very different from CPU code considerations

## Slide 7: Simulation Study
Want to better understand irregular apps’ specific demands on GPU hardware
  To help software developers optimize irregular codes
  As a baseline for exploring hardware support for broader classes of codes
GPGPU-Sim v3.2.1 + a few extra perf. counters
  GTX 480 (Fermi) configuration
  Added configuration variants to scale latency, bandwidth, cache size, etc.

## Slide 8: Applications from LonestarGPU Suite
Breadth-First Search (BFS)
  Label each node in graph with min level from start node
Barnes-Hut (BH)
  N-body algorithm using octree to decompose space around bodies
Mesh Refinement (DMR)
  Iteratively transform ‘bad’ triangles by retriangulating surrounding cavity
Minimum Spanning Tree (MST)
  Contract minimum edge until single node
Single-Source Shortest Paths (SSSP)
  Find shortest path to each node from source

## Slide 9: Applications from Other Sources
Semi-Regular
FP Compression (FPC)
  Lossless data compression for DP floating-point values
  Irregular control flow
Traveling Salesman (TSP)
  Find minimal tour in graph using iterative hill climbing
  Irregular memory accesses
Regular
N-Body (NB)
  N-body algorithm using all-to-all force calculation
Monte Carlo (MC)
  Evaluates fair call price for set of options
  CUDA SDK version
Inputs result in working set ≥5 times default L2 size

## Slide 10: Application Performance
Peak = 480 IPC
As expected, regular mostly means better performing
  BH is the exception: primary kernel regularized
Clear tendency for lower IPCs for irregular codes
  But no simple rule to delineate regular vs. irregular

## Slide 11: Branch Divergence
Active instructions at warp issue
  32 = no divergence
  Only one code <50% occupied
Theoretical speedup
  Assumes each issue had 32 active insts.

## Slide 12: Memory Coalescing
Avg # of memory accesses by each global/local ld/st
  >1 = uncoalesced
Percentage of stalls due to uncoalesced accesses
  Provides an upper bound on speedup

## Slide 13: Memory Coalescing
New configuration to artificially remove pipeline stall penalty from non-coalesced accesses
  With no further improvements to memory pipeline, with increased-capacity miss queues and MSHRs
  Not intended to model realistic improvement

## Slide 14: L2 and DRAM Latency
Scaled L2 hit and DRAM access latencies
  Doubled, halved, zeroed
Most benchmarks more sensitive to L2 latency
  Even with input sizes several times the L2 capacity

## Slide 15: Interconnect and DRAM Bandwidth
Halved/doubled interconnect (L2) bandwidth and DRAM bus width
Benchmark sensitivities similar to latency results
L2 large enough to keep sufficient warps ready

## Slide 16: Cache Behavior
Very high miss ratios (generally >50% in L1)
Irregular codes have much greater MPKI
  BFS & SSSP: lots of pointer-chasing, little spatial locality

## Slide 17: Cache Size Scaling
Halved, doubled both (data) cache sizes
Codes sensitive to interconnect bandwidth are also sensitive to L1D size
  BH tree prefixes: L2 better at exploiting locality in traversals
Most codes hurt more by smaller L2 than L1D

## Slide 18: Individual Application Analysis
Large memory access penalty in irregular apps
Divergence penalty less than we expected
Synchronization penalty also below expectation
Regular codes have mostly fully-occupied cycles
Computation pipeline hazards (rather than LS)

## Slide 19: Conclusions
Irregular codes
  More load imbalance, branch divergence, and uncoalesced memory accesses than regular codes
  Less branch divergence, synchronization, and atomics penalty than we expected
    Software designers successfully addressing these issues
To support irregular codes, architects should focus on improving memory-related slowdowns
  Improving L2 latency/bandwidth more important than improving DRAM latency/bandwidth

## Slide 20: Questions?
Acknowledgments
NSF Graduate Research Fellowship grant 1144466
NSF grants 1141022, 1217231, and 1438963
Grants and gifts from NVIDIA Corporation

## Slide 22: Related Work
Simulator-based characterization studies
  Bakhoda et al. (ISPASS’09), Goswami et al. (IISWC’10), Blem et al. (EAMA’11), Che et al. (IISWC’10), Lee and Wu (ISPASS’14)
    CUDA SDK, Rodinia, Parboil (no focus on irregularity)
  Meng et al. (ISCA’10) – dynamic warp hardware modification
PTX emulator studies (also SDK, Rodinia, Parboil)
  Kerr et al. (IISWC’09) – GPU Ocelot, Wu et al. (CACHES’11)
Hardware performance counters
  Burtscher et al. (IISWC’12) – LonestarGPU, Che et al. (IISWC’13)

## Slide 23: Input Sizes
Code | Input
BFS | NYC road network (~264K nodes, ~734K edges)
 | (working set = 3898 kB = 5.08x L2 size)
 | RMAT graph (250K nodes, 500K edges)
BH | 494K bodies, 1 time step
 | (working set = 7718 kB = 10.05x L2 size)
DMR | 50.4K nodes, ~100.3K triangles, maxfactor = 10
 | (working set w/ maxfactor 10 = 7840 kB = 10.2x L2 size)
 | 30K nodes, 60K triangles
MST | NYC road network (~264K nodes, ~734K edges)
 | (working set = 3898 kB = 5.08x L2 size)
 | RMAT graph (250K nodes, 500K edges)
SSSP | NYC road network (~264K nodes, ~734K edges)
 | (working set = 3898 kB = 5.08x L2 size)
 | RMAT graph (250K nodes, 500K edges)
FPC | obs_error dataset (60 MB), 30 blocks, 24 warps/block
 | num_plasma dataset (34 MB), 30 blocks, 24 warps/block
TSP | att48 (48 cities, 15K climbers)
 | eil51 (51 cities, 15K climbers)
NB | 23,040 bodies, 1 time step
MC | 256 options

## Slide 24: Secondary Inputs

## Slide 25: GPGPU-Sim Configurations
 | Latency |  | Bus width |  |  | L1D |  |  |  |  | L2 |  |  | 
 | ROP | DRAM | Ict | DRAM | CP | Sz (PS) | Sz (PL) | MQ | MS | MM | Size | MQ | MS | MM
Default | 240 | 200 | 32 | 4 | Y | 16 | 48 | 8 | 32 | 8 | 768 | 4 | 32 | 4
1/2x ROP | 120 | 200 | " | " | " | " | " | " | " | " | " | " | " | "
2x ROP | 480 | 200 | " | " | " | " | " | " | " | " | " | " | " | "
1/2x DRAM | 240 | 100 | " | " | " | " | " | " | " | " | " | " | " | "
2x DRAM | 240 | 400 | " | " | " | " | " | " | " | " | " | " | " | "
No Latency | 0 | 0 | " | " | " | " | " | " | " | " | " | " | " | "
1/2x L1D Cache | 240 | 200 | 32 | 4 | Y | 8 | 24 | 8 | 32 | 8 | 768 | 4 | 32 | 4
2x L1D Cache | " | " | " | " | " | 32 | 96 | " | " | " | " | " | " | "
1/2x L2 Cache | " | " | " | " | " | 16 | 48 | " | " | " | 384 | " | " | "
2x L2 Cache | " | " | " | " | " | " | " | " | " | " | 1536 | " | " | "
1/2x DRAM Bandwidth | 240 | 200 | " | 2 | Y | 16 | 48 | 8 | 32 | 8 | 768 | 4 | 32 | 4
2x DRAM Bandwidth | " | " | " | 8 | " | " | " | " | " | " | " | " | " | "
1/2x Ict + DRAM B/W | " | " | 16 | 2 | " | " | " | " | " | " | " | " | " | "
2x Ict + DRAM B/W | " | " | 64 | 8 | " | " | " | " | " | " | " | " | " | "
No Coalesce Penalty | 240 | 200 | 32 | 4 | N | 16 | 48 | 8 | 32 | 8 | 768 | 4 | 32 | 4
NCP + Impr L1 Miss | " | " | " | " | N | " | " | 16 | 64 | 16 | " | 4 | 32 | 4
NCP +Impr L1+L2 Miss | " | " | " | " | N | " | " | 16 | 64 | 16 | " | 8 | 64 | 8
Latencies represent number of shader core cycles. Cache sizes in kB. ROP=Raster Operations Pipeline (models L2 hit latency). Ict = Interconnect (flit size). CP=Coalesce penalty, PS = Prefer Shared Mem, PL = Prefer L1, MQ=Miss queue entries, MS=Miss status holding register entries, MM=Max MSHR merges |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 26: Issue Bin Priority