## Slide 1: Modeling HexNet in ACL2
Presentation by Ebele Esimai
ebele@cs.utexas.edu

## Slide 2: OUTLINE
Introduction into HexNet and its features
Implementation in ACL2
Packet movement in a sample network
Proof properties
Some ACL2 events

## Slide 3: HexNet
The network plan is based on a hexagonal topology, hence is called HexNet.
This hexagonal topology can also be seen in the connections in a brick wall
Notes: With the goal to verify asynchronous circuits, the Portland team have chosen too look into a network on a chip.
Data transfer in Asynchronous circuits are performed by local communication protocols.

## Slide 4: HexNet
Each node in the network is called a JUNCTION.
A Junction can either be
  REPEATER (degree of 3) : This accepts data and forwards it to its appropriate output.
  DESTINATION (degree of 1) : This is an entry or exit point in the network.
Usually, branching and merging in the network is two-way.
Therefore, data on only two input links compete for each output link and data on each input link can leave through only two possible output links.
Our goal : Modeling the high-level description of this network and packet movement in the network

## Slide 5: Features of the network
Arbitration : Correct decision behavior when data arrives on two input links at nearly the same time. Also, a mechanism for fairness is needed.
W
S
E

## Slide 6: Features of the network
Packet Routing: Packet coming through one input link has two possible output links to pass through. This decision is based on the comparison of the final destination and the current junction’s location.
W
E
S

## Slide 7: Implementation of HexNet in ACL2
The network is modeled as a graph
Addressing is based on a cartesian grid, as such, each junction is list of its x coordinate and its y coordinate
There are two links between any two connected junctions to represent data movement in each direction.
(0 2)
(2 2)
(4 2)
(6 2)
(8 2)
(10 2)
(12 2)
(6 0)
(2 4)
(3 4)
(4 3)
(8 3)
(10 4)
(11 4)
(0 6)
(2 6)
(4 6)
(4 7)
(6 6)
(8 6)
(8 7)
(10 6)
(12 6)

## Slide 8: Implementation of HexNet in ACL2
(defconst *network*
;; junct dest in out
'(((0 2) ((2 2) S20 S02))
((2 2) ((0 2) S02 S20)
((4 2) S42 S24)
((2 4) T24 T42))
((4 2) ((2 2) S24 S42)
((6 2) S64 S46)
((4 3) T23 T32))
((6 2) ((4 2) S46 S64)
((8 2) S86 S68)
((6 0) T02 T20))
((8 2) ((6 2) S68 S86)
((10 2) S108 S810)
((8 3) T83 T38))
…
(0 2)
(2 2)
(4 2)
(6 2)
(8 2)
(10 2)
(12 2)
(6 0)
(2 4)
(3 4)
(4 3)
(8 3)
(10 4)
(11 4)
(0 6)
(2 6)
(4 6)
(4 7)
(6 6)
(8 6)
(8 7)
(10 6)
(12 6)

## Slide 9: Packets
A packet is modelled as a list that contains
  A turn signal, which is the next direction the packet should take
  An address of final destination of the packet
  An address of the origin of the packet
  The information to be passed along
The packets are stored on the links.
A link can either be full or empty.
A linkmap shows the current state of all the links in the network at a given time.
Pkt1 - ‘(E (8 7) (0 2) data)
E – turn_signal
(8 7) – coordinates of the final destination
(0 2) – coordinates of the origin of the packet
(defconst *linkmap*
'((S02 (E (12 2) (0 2) data))
(S20) (S24) (S42) (S46) (S64)
(S68) (S86) (S810) (S108)
(S1012) (S1220) (T20)
(T02) (T32) (T23) (T38)
(T83 (W (3 4) (8 3) data)) …

## Slide 10: Arbitration in the Model
Arbitration is based on the output direction
One of the packets is chosen to proceed while the second waits
W
S
E
pkt1
pkt2
W
S
E
pkt1
pkt2
Notes: If pkt1 and pkt2 arrive nearly at the same time with both having to move East,

## Slide 11: Arbitration in the Model
Arbitration is based on the output direction
One of the packets is chosen to proceed while the second waits
However, to facilitate fairness, the model has to remember the decision at the previous step if there is another tie at that junction
W
S
E
pkt3
pkt2
W
S
E
pkt3
pkt2

## Slide 12: Arbitration in the Model
Arbitration is based on the output direction
One of the packets is chosen to proceed while the second waits
However, to facilitate fairness, the model has to remember the decision at the previous step if there is another tie at that junction
Outlink – link in the output direction
Inputs – links with packets
St – statemap that stores previous step decisions
(defun arbiter (outlink inputs st)
(cond
((atom inputs) (mv nil st))
((atom (cdr inputs)) (mv (car inputs) st))
(t (let* ((entry (assoc-eq outlink st))
(pref (cdr entry)))
(if (and pref
(member-eq pref inputs))
(let* ((new-pref (car (remove-eq pref inputs)))
(new-st (update-alist outlink new-pref st)))
(mv pref new-st))
(let* ((new-pref (cadr inputs))
(new-st (update-alist outlink new-pref st)))
(mv (car inputs) new-st)))))))

## Slide 13: Packet Routing
The network uses Advanced Address Decoding
This means that the routing function calculates the next direction, i.e. turn-signal, a step before it makes the turn.
Comparison is made between the final destination of the packet and the address of next junction.
Turn_signal (pkt1) = East => curr
Routing_function (dest1 dest2 curr final g) = (compare curr final) => East or South
dest1
dest2
curr
pkt1

## Slide 14: Routing Packet Traffic
(defun routing-normal (dest1 dest2 curr final g)
(let* ((dest1-x (car dest1)) (dest1-y (cadr dest1) (dest2-x (car dest2))
(dir1 (get-direction curr dest1 g)) (dir2 (get-direction curr dest2 g))
(curr-x (car curr)) (curr-y (cadr curr))
(final-x (car final)) (final-y (cadr final)))
(if (isTerminal dest1 curr g)
(if (equal dest1 final) dir1
(if (isTerminal dest2 curr g)
(if (equal dest2 final) dir2 (cw "Bad route "))
dir2))
(if (isTerminal dest2 curr g)
(if (equal dest2 final) dir2 dir1)
(cond ((< curr-y final-y)
(if (< curr-y dest1-y) dir1 dir2))
((> curr-y final-y)
(if (> curr-y dest1-y) dir1 dir2))
((< curr-x final-x)
(if (< dest1-x dest2-x) dir2 dir1))
((> curr-x final-x)
(if (< dest1-x dest2-x) dir1 dir2)))))))
pkt1
dest1
dest2
curr

## Slide 15: Example
Linkmap before execution
(S02 (E (12 2) (0 2) data))
(T83 (W (3 4) (8 3) data))
(T68 (E (12 2) (6 8) data))
(6 8)
(0 2)
(2 2)
(4 2)
(6 2)
(8 2)
(10 2)
(12 2)
(6 0)
(2 4)
(3 4)
(4 3)
(8 3)
(10 4)
(11 4)
(0 6)
(2 6)
(4 6)
(4 7)
(6 6)
(8 6)
(8 7)
(10 6)
(12 6)
pkt1
pkt2
pkt3

## Slide 16: Example
Linkmap before execution
(S02 (E (12 2) (0 2) data))
(T83 (W (3 4) (8 3) data))
(T68 (E (12 2) (6 8) data))
Linkmap after 1 step
(S24 (E (12 2) (0 2) DATA))
(S86 (W (3 4) (8 3) DATA))
(S686 (E (12 2) (6 8) DATA))
(6 8)
(0 2)
(2 2)
(4 2)
(6 2)
(8 2)
(10 2)
(12 2)
(6 0)
(2 4)
(3 4)
(4 3)
(8 3)
(10 4)
(11 4)
(0 6)
(2 6)
(4 6)
(4 7)
(6 6)
(8 6)
(8 7)
(10 6)
(12 6)
pkt1
pkt2
pkt3

## Slide 17: Example
Linkmap before execution
(S02 (E (12 2) (0 2) data))
(T83 (W (3 4) (8 3) data))
(T68 (E (12 2) (6 8) data))
Linkmap after 1 step
(S24 (E (12 2) (0 2) DATA))
(S86 (W (3 4) (8 3) DATA))
(S686 (E (12 2) (6 8) DATA))
Linkmap after 2 steps
(S46 (E (12 2) (0 2) DATA))
(S64 (W (3 4) (8 3) DATA))
(S610 (S (12 2) (6 8) DATA))
(6 8)
(0 2)
(2 2)
(4 2)
(6 2)
(8 2)
(10 2)
(12 2)
(6 0)
(2 4)
(3 4)
(4 3)
(8 3)
(10 4)
(11 4)
(0 6)
(2 6)
(4 6)
(4 7)
(6 6)
(8 6)
(8 7)
(10 6)
(12 6)
pkt1
pkt2
pkt3

## Slide 18: Example
Linkmap before execution
(S02 (E (12 2) (0 2) data))
(T83 (W (3 4) (8 3) data))
(T68 (E (12 2) (6 8) data))
Linkmap after 1 step
(S24 (E (12 2) (0 2) DATA))
(S86 (W (3 4) (8 3) DATA))
(S686 (E (12 2) (6 8) DATA))
Linkmap after 2 steps
(S46 (E (12 2) (0 2) DATA))
(S64 (W (3 4) (8 3) DATA))
(S610 (S (12 2) (6 8) DATA))
Linkmap after 3 steps
(S68 (E (12 2) (0 2) DATA))
(S42 (N (3 4) (8 3) DATA))
(T106 (S (12 2) (6 8) DATA))
(6 8)
(0 2)
(2 2)
(4 2)
(6 2)
(8 2)
(10 2)
(12 2)
(6 0)
(2 4)
(3 4)
(4 3)
(8 3)
(10 4)
(11 4)
(0 6)
(2 6)
(4 6)
(4 7)
(6 6)
(8 6)
(8 7)
(10 6)
(12 6)
pkt1
pkt2
pkt3

## Slide 19: Example
Linkmap before execution
(S02 (E (12 2) (0 2) data))
(T83 (W (3 4) (8 3) data))
(T68 (E (12 2) (6 8) data))
Linkmap after 1 step
(S24 (E (12 2) (0 2) DATA))
(S86 (W (3 4) (8 3) DATA))
(S686 (E (12 2) (6 8) DATA))
Linkmap after 2 steps
(S46 (E (12 2) (0 2) DATA))
(S64 (W (3 4) (8 3) DATA))
(S610 (S (12 2) (6 8) DATA))
Linkmap after 3 steps
(S68 (E (12 2) (0 2) DATA))
(S42 (N (3 4) (8 3) DATA))
(T106 (S (12 2) (6 8) DATA))
Linkmap after 4 steps
(S810 (E (12 2) (0 2) DATA))
(T42 (E (3 4) (8 3) DATA))
(T104 (E (12 2) (6 8) DATA))
(6 8)
(0 2)
(2 2)
(4 2)
(6 2)
(8 2)
(10 2)
(12 2)
(6 0)
(2 4)
(3 4)
(4 3)
(8 3)
(10 4)
(11 4)
(0 6)
(2 6)
(4 6)
(4 7)
(6 6)
(8 6)
(8 7)
(10 6)
(12 6)
pkt1
pkt2
pkt3

## Slide 20: Example
Linkmap after 4 steps
(S810 (E (12 2) (0 2) DATA))
(T42 (E (3 4) (8 3) DATA))
(T104 (E (12 2) (6 8) DATA))
Linkmap after 5 steps
(S1012 (DONE (12 2) (0 2) DATA))
(S23 (DONE (3 4) (8 3) DATA))
(T104 (E (12 2) (6 8) DATA))
The statemap records that preference should be given to pkt2 if there is a tie in the next step.
(S1012 . T104)
(6 8)
(0 2)
(2 2)
(4 2)
(6 2)
(8 2)
(10 2)
(12 2)
(6 0)
(2 4)
(3 4)
(4 3)
(8 3)
(10 4)
(11 4)
(0 6)
(2 6)
(4 6)
(4 7)
(6 6)
(8 6)
(8 7)
(10 6)
(12 6)
pkt1
pkt2
pkt3

## Slide 21: Example
Linkmap after 4 steps
(S810 (E (12 2) (0 2) DATA))
(T42 (E (3 4) (8 3) DATA))
(T104 (E (12 2) (6 8) DATA))
Linkmap after 5 steps
(S1012 (DONE (12 2) (0 2) DATA))
(S23 (DONE (3 4) (8 3) DATA))
(T104 (E (12 2) (6 8) DATA))
The statemap records that preference should be given to pkt2 if there is a tie in the next step.
(S1012 . T104)
Linkmap after 6 steps
(S1012 (DONE (12 2) (6 8) DATA))
(6 8)
(0 2)
(2 2)
(4 2)
(6 2)
(8 2)
(10 2)
(12 2)
(6 0)
(2 4)
(3 4)
(4 3)
(8 3)
(10 4)
(11 4)
(0 6)
(2 6)
(4 6)
(4 7)
(6 6)
(8 6)
(8 7)
(10 6)
(12 6)
pkt2

## Slide 22: Proof Properties
Reachability: Every information source can send data to every destination.
Diameter: The number of steps that the communication from source to destination will take

## Slide 23
(defun update-link (junct dest lt st g) “Calculates update for the next link”
(let* ((outlink (outlink-lookup junct dest g)))
(if (cdr (assoc-eq outlink lt))
(if (equal (car (cadr (assoc-eq outlink lt))) 'Done)
(let ((new-lt (update-alist outlink nil lt)))
(mv new-lt st))
(mv lt st))
(let* ((stack (remove-equal dest (sources junct g)))
(inputs (current-inputs junct dest stack lt g)))
(if (endp inputs)
(mv lt st)
(let* ((result (mv-list 2 (oracle outlink inputs st)))
(input (car result))
(new-st (cadr result)))
(if (atom (cdr (assoc-eq input lt)))
(mv nil nil)
(let* ((pkt (cadr (assoc-eq input lt)))
(final (cadr pkt))
(turn_signal (routing junct dest final g)))
(if turn_signal
(let* ((new-pkt (cons turn_signal (cdr pkt)))
(new-link-state (update-alist outlink (list new-pkt) lt))
(new-lt (update-alist input nil new-link-state)))
(mv new-lt new-st))
(mv nil nil))))))))))

## Slide 24
(defun step-junct (junct neighbors lt st g) “Updates all output links in a junction”
(if (endp neighbors)
(mv lt st)
(let ((dest (car neighbors)))
(if (junctp dest g)
(let* ((result (mv-list 2 (update-link junct dest lt st g)))
(new-lt (car result))
(new-st (cadr result)))
(step-junct junct (cdr neighbors) new-lt new-st g))
(mv nil nil)))))
(defun run (juncts lt st g) “Updates the Junctions by a step”
(if (endp juncts)
(mv lt st)
(let* ((junct (car juncts))
(neighbors (sources junct g))
(result (mv-list 2 (step-junct junct neighbors lt st g)))
(new-lt (car result))
(new-st (cadr result)))
(run (cdr juncts) new-lt new-st g))))