## Slide 1: Lecture 7: Advanced BGP Concepts
Lecturer: Venkat Arun
Note: A lot of what we discuss today is not in the book. I have included references where relevant

## Slide 2: Logistics
The deadline on the website is correct. Assignment 2 is not due tomorrow! Sorry about that
Reminder: quiz next Thursday
  One page of notes are allowed but will probably not be necessary. If you are missing some information, just ask us. We’ll tell you. You are only responsible for conceptual understanding and reasoning

## Slide 3: Recap
ASes advertise routes to each other.
  Suppose A tells (advertises to) B about a route to IP prefix X (e.g. 128.3.0.0/16)
  The route advertisement consists of the sequence of ASes through which the packet will be sent if B were to send A an IP packet with destination address in X
An AS may have received multiple advertisements to the same IP address. For a given address (or more likely, a given IP prefix), the AS can pick any route it likes
Once it has picked a route, it starts sending packets over that route and advertises the others and withdraws previous routes if any
  To a given AS B, AS A will advertise only one route to any prefix X. Exception is if the ASes are connected via multiple routers, in which case it can send one advertisement per connection point

## Slide 4: Multiple connections between two ASes
Microsoft
AT&T
Seattle
Austin
Spectrum Internet
Connection point 1
Connection point 2
AT&T makes two advertisements to Spectrum, one for each connection point
It indicates its preference for which connection to use
  It will probably prefer connection 2 since that is less work
Microsoft may choose to respect or ignore that preference. If AT&T really does not want Microsoft to use connection 1, then it should not advertise it
  It is cheaper for Microsoft to use connection 1
  Using connection 2 might give the user better quality of Microsoft’s network is better. It does something in a similar spirit for Microsoft Teams calls

## Slide 5: Clever ways to “misuse” BGP features
If you want to tell someone else to deprioritize using a path you just advertised, just pad the length. E.g. say “AS10 AS3 AS3 AS3 AS400”
If you want to load balance between multiple entry points, split up the IP prefix into different groups and make separate advertisements. For example:
  128.9.0.0/18 can be reached via entry 1 through path AS10 AS3 AS400
  128.9.0.1/18 can be reached via entry 1 through path AS10 AS3 AS400
  128.9.0.2/18 can be reached via entry 1 through path AS10 AS3 AS400
  128.9.0.3/18 can be reached via entry 1 through path AS10 AS3 AS400

## Slide 6: Example algorithm to pick routes
ASes are free to pick any route they like. However, most use algorithms implemented by companies like Cisco and configure it to their needs. For example:
AS
Refer: https://community.cisco.com/t5/networking-knowledge-base/understanding-bgp-best-path-selection-manipulation/ta-p/3150576

## Slide 7: Will BGP routes converge?
Slides borrowed from Jen Rexford’s talk: https://slideplayer.com/slide/5073626/
The paper she wrote with Lixin Gao called “Stable Internet Routing Without Global Coordination” forms a crucial part of our understanding of the internet

## Slide 8: BGP does not converge
0
1
2
3
1 2 0
1 0
2 3 0
2 0
3 1 0
3 0
Pick the highest-ranked path consistent with your neighbors’ choices.
Only choice!
Top choice!
Only choice!
Better choice!
Only choice!
Better choice!

## Slide 9: Instapoll Quiz: Which of the following is stable?
0
1
2
3
1 0
1 2 0
2 3 0
2 0
3 1 0
3 0
0
1
2
3
1 0
1 2 0
2 0
2 3 0
3 0
3 1 0
0
1
2
3
1 0
2 0
3 0
A
B
C

## Slide 10: Global Control is Not Workable
Create a global Internet routing registry
  Difficult to keep up to date
Require each AS to publish its routing policies
  Difficult to get them to participate
Check for conflicting policies, and resolve conflicts
  Re-checking for each failure scenario
Need a solution that does not require global coordination.

## Slide 11: Global Control is Not Workable
Create a global Internet routing registry
  Difficult to keep up to date
Require each AS to publish its routing policies
  Difficult to get them to participate
Check for conflicting policies, and resolve conflicts
  Checking is NP-complete
  Re-checking for each failure scenario
Need a solution that does not require global coordination.

## Slide 12: Think Globally, Act Locally
Design goals
  Flexibility: allow complex local policies
  Privacy: do not require divulging policies
  Backwards-compatibility: no changes to the protocol
  Guarantees: convergence even when system changes
Solution: restrictions based on AS relationships
  Path selection rules: which route you prefer
  Export policies: who you tell about your route
  AS graph structure: who is connected to who

## Slide 13: Customer-Provider Relationship
Customer pays provider for access to the Internet
  Provider exports its customer’s routes to everybody
  Customer exports provider’s routes only to its customers
d
d
AT&T
Princeton
Princeton
AT&T
Traffic to the customer
Traffic from the customer
advertisements
traffic

## Slide 14: Peer-Peer Relationship
Peers exchange traffic between their customers
  AS exports only customer routes to a peer
  AS exports a peer’s routes only to its customers
DT
AT&T
Traffic to/from the peer and its customers
d
advertisements
traffic
Princeton
MPI

## Slide 15: Hierarchical AS Relationships
Provider-customer graph is a directed, acyclic graph
  If u is a customer of v and v is a customer of w
  … then w is not a customer of u
u
v
w

## Slide 16: Proposed Local Path Selection Rules
Classify routes based on next-hop AS
  Customer routes, peer routes, and provider routes
Rank routes based on classification
  Prefer customer routes over peer and provider routes
Allow any ranking of routes within a class
  E.g., do not impose ranking among customer routes
Consistent with economic incentives
  Customers pay for service, and providers are paid
  Peer relationship contingent on balanced traffic load
If everyone follows these rules, the system will converge

## Slide 17: Solving the Convergence Problem
Assumptions
  Export policies based on AS relationships
  Path selection rule that favors customer routes
  Acyclic provider-customer graph
Result
  Guaranteed convergence of the routing protocol
  Holds under link/router failures and policy changes
Sketch of (constructive) proof
  Activation sequence that leads to a stable state
  Any “fair” activation sequence includes this sequence

## Slide 18: Proof, Phase 1: Selecting Customer Routes
Activate ASes in customer-provider order
  AS picks a customer route if one exists
  Decision of one AS cannot cause an earlier AS to change its mind
0
1
2
3
d
An AS picks a customer
route when one exists

## Slide 19: Proof, Phase 2: Selecting Peer and Provider Routes
Activate rest of ASes in provider-customer order
  Decision of one phase-2 AS cannot cause an earlier phase-2 AS to change its mind
  Decision of phase-2 AS cannot affect a phase 1 AS
0
1
2
3
8
7
6
5
4
AS picks a peer or provider
route when no customer
route is available
d

## Slide 20: Economic Incentives Affect Protocol Behavior
ASes already follow our rules, so system is stable
  High-level argument
    Export and topology assumptions are reasonable
    Path-selection rule matches economic incentives
  Empirical results
    Routes for popular destinations are stable for ~10 days
    Most churn due to small number of unpopular destinations
ASes should follow our rules to make system stable
  Encourage operators to obey these guidelines
  … and provide configuration-checking tools
  Consider more complex relationships and graphs

## Slide 21: Different Rules: More Flexible Import Policies
Allowing more flexibility in ranking routes
  Allow the same rank for peer and customer routes with the same AS path length
  Never choose a peer route over a shorter customer route
Stricter AS graph assumptions
  Hierarchical provider-customer relationship (as before)
  No private peering with (direct or indirect) providers
Peer-peer

## Slide 22: Backup Relationships
Backups: more liberal export policies
  Primary and a backup provider
  Peers giving backup service to each other
Extension: prefer routes with fewest backup links
backup path
primary
provider
backup
provider
failure
Backup Provider
backup path
failure
peer
provider
Peer-Peer Backup

## Slide 23: Conclusions on Guaranteed Convergence
Avoiding convergence problems
  Hierarchical AS relationships
  Export policies based on commercial relationships
  Guidelines for import policies based on relationships
Salient features
  No global coordination (locally implementable)
  No changes to BGP protocol or decision process
  Guaranteed convergence, even under failures
  Guidelines consistent with economic incentives

## Slide 24: Recent Work Building on the Policy Guidelines
AS relationships and BGP convergence
  Design principles for policy languages
  Fundamental limits on relaxing the assumptions
Internal BGP inside an AS
  Sufficient conditions for iBGP convergence
  “What-if” tool for traffic engineering
AS-level analysis of the Internet
  Inference of AS relationships from routing data
  Characterization of AS-level topology and growth
Network design and operations
  Analyzing competitors and changing BGP policies
  Setting protective route filters on BGP sessions

## Slide 25: Open Problems in Economic Incentives in Interdomain Routing

## Slide 26: Models of How Relationships Form and Operate
Selecting a peer
  Motivation: basic reachability and reducing transit costs
  Making a peer pay when they need you (slightly) more
  De-peering, refusing to peer, and stealing customers
  Peer AS in one part of the world, but provider in another
Selecting a provider
  Motivation: cost, performance, and physical proximity
  Multi-homing to game one provider against another
  Using third-party aggregators that negotiate with ISPs

## Slide 27: Negotiation for Better Egress Selection
Better to cooperate
  Negotiate where to send
  Inbound and outbound
  Mutual benefits
But, how to do it?
  What info to exchange?
  How to prioritize the many choices?
  How prevent cheating?
Customer A
Customer B
multiple
peering
points
Provider A
Provider B
Early-exit
routing

## Slide 28: Reducing Vulnerability to Misbehaving Domains
1
2
3
4
5
6
7
12.34.0.0/16
12.34.0.0/16
Interdomain routing depends on trust
  Vulnerable to malicious attack or accidental misconfiguration
  Prefix hijacks lead to black hole, snooping, or impersonation

## Slide 29: Stepping Back: Where Should the Incentives Go?
Today’s interdomain routing
  Incentives do not live inside the protocol
  But, rather, in how the policies are configured
  However, this is indirect and perhaps even unnatural
Other possibilities…
  Advertise policy preferences and options
  Associate prices with route advertisements
  Support negotiation between neighboring ASes
  <Your solution here>

## Slide 30: Bad news travels slowly in BGP too
… but not as slowly as in distance vector routing since it can detect loops
We will not cover this in this course, but if you are interested, it is called “BGP path hunting”
Here is a good resource: https://www.noction.com/blog/bgp-path-hunting

## Slide 31: Recall: forwarding
Thus far, we have discussed routing algorithms. Together, these populate “forwarding tables” in each router
A forwarding table specifies, for each IP prefix, on which port the router should forward the packet (note, here “port” refers to a physical device. Not to be confused with TCP/UDP port numbers)
When a routers receives a packet, if multiple rows match the destination IP address, it picks the one with the longest prefix
IP Address | Mask | Next Hop
128.62.0.0/16 | 255.255.0.0 | Port 1
18.0.0.0/9 | 255.128.0.0 | Port 2
18.128.0.0/9 | 255.128.0.0 | Port 3
162.9.1.0/24 | 255.255.255.0 | Port 1

## Slide 32: Forwarding is hard too
If a router supports 100 Gbit/s link, and the maximum transmission unit (MTU) is 1500 bytes, that is just 12 us/packet
If all packets are small, say 40 bytes, that is just 3.2 ns/packet!
  This is not uncommon
Some routers can have a million entries in its routing table
Doing longest prefix matching at such a high rate is quite challenging. Fortunately, different packets can be matched in parallel
Often dedicated hardware is used to perform this matching
We will not discuss forwarding algorithms/datastructures further in this course

## Slide 33: Let’s recap
And study a Facebook outage in 2024 (back when they were still called “Facebook”)

## Slide 34
Give me my messages
There you go
Notes: <div>Icons made by <a href="https://www.freepik.com" title="Freepik">Freepik</a> from <a href="https://www.flaticon.com/" title="Flaticon">www.flaticon.com</a></div>

## Slide 35
Internet
Notes: <div>Icons made by <a href="https://www.freepik.com" title="Freepik">Freepik</a> from <a href="https://www.flaticon.com/" title="Flaticon">www.flaticon.com</a></div>

## Slide 36
157.240.192.35
142.251.33.78
18.31.7.218
Notes: <div>Icons made by <a href="https://www.freepik.com" title="Freepik">Freepik</a> from <a href="https://www.flaticon.com/" title="Flaticon">www.flaticon.com</a></div>

## Slide 37
157.240.192.35
142.251.33.78
18.31.7.218
To: 157.240.192.35
Message: “Give me my messages”
Notes: <div>Icons made by <a href="https://www.freepik.com" title="Freepik">Freepik</a> from <a href="https://www.flaticon.com/" title="Flaticon">www.flaticon.com</a></div>

## Slide 38
157.240.192.35
142.251.33.78
18.31.7.218
facebook.com
Address book
Notes: <div>Icons made by <a href="https://www.freepik.com" title="Freepik">Freepik</a> from <a href="https://www.flaticon.com/" title="Flaticon">www.flaticon.com</a></div>

## Slide 39
157.240.192.35
142.251.33.78
18.31.7.218
facebook.com
Address book
157.240.192.35
Notes: <div>Icons made by <a href="https://www.freepik.com" title="Freepik">Freepik</a> from <a href="https://www.flaticon.com/" title="Flaticon">www.flaticon.com</a></div>

## Slide 40
Address book
Address book
Address book
Local
Address book
Less local
Cannot find!

## Slide 41
Your ISP
Address book
I can reach:
Facebook’s address book
Facebook’s web-server
...
I can reach:
Google’s address book
Google’s web-server
...
I can reach:
Facebook’s address book
Facebook’s web-server
Google’s address book
Google’s web server

## Slide 42
Your ISP
Address book
I can reach:
Facebook’s address book
Facebook’s web-server
...
I can reach:
Google’s address book
Google’s web-server
...
I can reach:
Facebook’s address book
Facebook’s web-server
Google’s address book
Google’s web server

## Slide 43
Your ISP
Address book
I can reach:
Facebook’s address book
Facebook’s web-server
...
I can reach:
Google’s address book
Google’s web-server
...
I can reach:
Facebook’s address book
Facebook’s web-server
Google’s address book
Google’s web server