## Slide 1: Datapath Design II
Topics
  Control flow instructions
  Hardware for sequential machine (SEQ)
Systems I

## Slide 2: Executing Jumps
Fetch
  Read 5 bytes
  Increment PC by 5
Decode
  Do nothing
Execute
  Determine whether to take branch based on jump condition and condition codes
Memory
  Do nothing
Write back
  Do nothing
PC Update
  Set PC to Dest if branch taken or to incremented PC if not branch
jXX Dest
7
fn
Dest
XX
XX
fall thru:
XX
XX
target:
Not taken
Taken

## Slide 3: Stage Computation: Jumps
  Compute both addresses
  Choose based on setting of condition codes and branch condition
jXX Dest
icode:ifun  M1[PC]
valC  M4[PC+1]
valP  PC+5
Fetch
Read instruction byte
Read destination address
Fall through address
Decode
Bch  Cond(CC,ifun)
Execute
Take branch?
Memory
Write
back
PC  Bch ? valC : valP
PC update
Update PC

## Slide 4: Executing call
Fetch
  Read 5 bytes
  Increment PC by 5
Decode
  Read stack pointer
Execute
  Decrement stack pointer by 4
Memory
  Write incremented PC to new value of stack pointer
Write back
  Update stack pointer
PC Update
  Set PC to Dest
call Dest
8
0
Dest
XX
XX
return:
XX
XX
target:

## Slide 5: Stage Computation: call
  Use ALU to decrement stack pointer
  Store incremented PC
call Dest
icode:ifun  M1[PC]
valC  M4[PC+1]
valP  PC+5
Fetch
Read instruction byte
Read destination address
Compute return point
valB  R[%esp]
Decode
Read stack pointer
valE  valB + –4
Execute
Decrement stack pointer
M4[valE]  valP
Memory
Write return value on stack
R[%esp]  valE
Write
back
Update stack pointer
PC  valC
PC update
Set PC to destination

## Slide 6: Executing ret
Fetch
  Read 1 byte
Decode
  Read stack pointer
Execute
  Increment stack pointer by 4
Memory
  Read return address from old stack pointer
Write back
  Update stack pointer
PC Update
  Set PC to return address
ret
9
0
XX
XX
return:

## Slide 7: Stage Computation: ret
  Use ALU to increment stack pointer
  Read return address from memory
ret
icode:ifun  M1[PC]
Fetch
Read instruction byte
valA  R[%esp]
valB  R[%esp]
Decode
Read operand stack pointer
Read operand stack pointer
valE  valB + 4
Execute
Increment stack pointer
valM  M4[valA]
Memory
Read return address
R[%esp]  valE
Write
back
Update stack pointer
PC  valM
PC update
Set PC to return address

## Slide 8: Computation Steps
  All instructions follow same general pattern
  Differ in what gets computed on each step
OPl rA, rB
icode:ifun  M1[PC]
rA:rB  M1[PC+1]
valP  PC+2
Fetch
Read instruction byte
Read register byte
[Read constant word]
Compute next PC
valA  R[rA]
valB  R[rB]
Decode
Read operand A
Read operand B
valE  valB OP valA
Set CC
Execute
Perform ALU operation
Set condition code register
Memory
[Memory read/write]
R[rB]  valE
Write
back
Write back ALU result
[Write back memory result]
PC  valP
PC update
Update PC
icode,ifun
rA,rB
valC
valP
valA, srcA
valB, srcB
valE
Cond code
valM
dstE
dstM
PC

## Slide 9: Computation Steps
  All instructions follow same general pattern
  Differ in what gets computed on each step
call Dest
Fetch
Decode
Execute
Memory
Write
back
PC update
icode,ifun
rA,rB
valC
valP
valA, srcA
valB, srcB
valE
Cond code
valM
dstE
dstM
PC
icode:ifun  M1[PC]
valC  M4[PC+1]
valP  PC+5
valB  R[%esp]
valE  valB + –4
M4[valE]  valP
R[%esp]  valE
PC  valC
Read instruction byte
[Read register byte]
Read constant word
Compute next PC
[Read operand A]
Read operand B
Perform ALU operation
[Set condition code reg.]
[Memory read/write]
[Write back ALU result]
Write back memory result
Update PC

## Slide 10: Computed Values
Fetch
  icode Instruction code
  ifun Instruction function
  rA Instr. Register A
  rB Instr. Register B
  valC Instruction constant
  valP Incremented PC
Decode
  srcA Register ID A
  srcB Register ID B
  dstE Destination Register E
  dstM Destination Register M
  valA Register value A
  valB Register value B
Execute
  valE ALU result
  Bch Branch flag
Memory
  valM Value from memory

## Slide 11: SEQ Hardware
Key
  Blue boxes: predesigned hardware blocks
    E.g., memories, ALU
  Gray boxes: control logic
    Describe in HCL
  White ovals: labels for signals
  Thick lines: 32-bit word values
  Thin lines: 4-8 bit values
  Dotted lines: 1-bit values

## Slide 12: Summary
Today
  Control flow instructions
  Hardware for sequential machine (SEQ)
Next time
  Control logic for instruction execution
  Timing and clocking

## Slide 13: Datapath Design III
Topics
  Control logic for instruction execution
  Timing and clocking
Systems I

## Slide 14: Fetch Logic
Predefined Blocks
  PC: Register containing PC
  Instruction memory: Read 6 bytes (PC to PC+5)
  Split: Divide instruction byte into icode and ifun
  Align: Get fields for rA, rB, and valC

## Slide 15: Fetch Logic
Control Logic
  Instr. Valid: Is this instruction valid?
  Need regids: Does this instruction have a register byte?
  Need valC: Does this instruction have a constant word?

## Slide 16: Fetch Control Logic
bool need_regids =
icode in { IRRMOVL, IOPL, IPUSHL, IPOPL,
IIRMOVL, IRMMOVL, IMRMOVL };
bool instr_valid = icode in
{ INOP, IHALT, IRRMOVL, IIRMOVL, IRMMOVL, IMRMOVL,
IOPL, IJXX, ICALL, IRET, IPUSHL, IPOPL };

## Slide 17: Decode Logic
Register File
  Read ports A, B
  Write ports E, M
  Addresses are register IDs or 8 (no access)
Control Logic
  srcA, srcB: read port addresses
  dstA, dstB: write port addresses

## Slide 18: A Source
OPl rA, rB
valA  R[rA]
Decode
Read operand A
rmmovl rA, D(rB)
valA  R[rA]
Decode
Read operand A
popl rA
valA  R[%esp]
Decode
Read stack pointer
jXX Dest
Decode
No operand
call Dest
valA  R[%esp]
Decode
Read stack pointer
ret
Decode
No operand
int srcA = [
icode in { IRRMOVL, IRMMOVL, IOPL, IPUSHL } : rA;
icode in { IPOPL, IRET } : RESP;
1 : RNONE; # Don't need register
];

## Slide 19: E Destination
None
R[%esp]  valE
Update stack pointer
None
R[rB]  valE
OPl rA, rB
Write-back
rmmovl rA, D(rB)
popl rA
jXX Dest
call Dest
ret
Write-back
Write-back
Write-back
Write-back
Write-back
Write back result
R[%esp]  valE
Update stack pointer
R[%esp]  valE
Update stack pointer
int dstE = [
icode in { IRRMOVL, IIRMOVL, IOPL} : rB;
icode in { IPUSHL, IPOPL, ICALL, IRET } : RESP;
1 : RNONE; # Don't need register
];

## Slide 20: Execute Logic
Units
  ALU
    Implements 4 required functions
    Generates condition code values
  CC
    Register with 3 condition code bits
  bcond
    Computes branch flag
Control Logic
  Set CC: Should condition code register be loaded?
  ALU A: Input A to ALU
  ALU B: Input B to ALU
  ALU fun: What function should ALU compute?

## Slide 21: ALU A Input
valE  valB + –4
Decrement stack pointer
No operation
valE  valB + 4
Increment stack pointer
valE  valB + valC
Compute effective address
valE  valB OP valA
Perform ALU operation
OPl rA, rB
Execute
rmmovl rA, D(rB)
popl rA
jXX Dest
call Dest
ret
Execute
Execute
Execute
Execute
Execute
valE  valB + 4
Increment stack pointer
int aluA = [
icode in { IRRMOVL, IOPL } : valA;
icode in { IIRMOVL, IRMMOVL, IMRMOVL } : valC;
icode in { ICALL, IPUSHL } : -4;
icode in { IRET, IPOPL } : 4;
# Other instructions don't need ALU
];

## Slide 22: ALU Operation
valE  valB + –4
Decrement stack pointer
No operation
valE  valB + 4
Increment stack pointer
valE  valB + valC
Compute effective address
valE  valB OP valA
Perform ALU operation
OPl rA, rB
Execute
rmmovl rA, D(rB)
popl rA
jXX Dest
call Dest
ret
Execute
Execute
Execute
Execute
Execute
valE  valB + 4
Increment stack pointer
int alufun = [
icode == IOPL : ifun;
1 : ALUADD;
];

## Slide 23: Memory Logic
Memory
  Reads or writes memory word
Control Logic
  Mem. read: should word be read?
  Mem. write: should word be written?
  Mem. addr.: Select address
  Mem. data.: Select data

## Slide 24: Memory Address
OPl rA, rB
Memory
rmmovl rA, D(rB)
popl rA
jXX Dest
call Dest
ret
No operation
M4[valE]  valA
Memory
Write value to memory
valM  M4[valA]
Memory
Read from stack
M4[valE]  valP
Memory
Write return value on stack
valM  M4[valA]
Memory
Read return address
Memory
No operation
int mem_addr = [
icode in { IRMMOVL, IPUSHL, ICALL, IMRMOVL } : valE;
icode in { IPOPL, IRET } : valA;
# Other instructions don't need address
];

## Slide 25: Memory Read
OPl rA, rB
Memory
rmmovl rA, D(rB)
popl rA
jXX Dest
call Dest
ret
No operation
M4[valE]  valA
Memory
Write value to memory
valM  M4[valA]
Memory
Read from stack
M4[valE]  valP
Memory
Write return value on stack
valM  M4[valA]
Memory
Read return address
Memory
No operation
bool mem_read = icode in { IMRMOVL, IPOPL, IRET };

## Slide 26: PC Update Logic
New PC
  Select next value of PC

## Slide 27: PC Update
OPl rA, rB
rmmovl rA, D(rB)
popl rA
jXX Dest
call Dest
ret
PC  valP
PC update
Update PC
PC  valP
PC update
Update PC
PC  valP
PC update
Update PC
PC  Bch ? valC : valP
PC update
Update PC
PC  valC
PC update
Set PC to destination
PC  valM
PC update
Set PC to return address
int new_pc = [
icode == ICALL : valC;
icode == IJXX && Bch : valC;
icode == IRET : valM;
1 : valP;
];

## Slide 28: SEQ Operation
State
  PC register
  Cond. Code register
  Data memory
  Register file
  All updated as clock rises
Combinational Logic
  ALU
  Control logic
  Memory reads
    Instruction memory
    Register file
    Data memory

## Slide 29: SEQ Operation #2
  state set according to second irmovl instruction
  combinational logic starting to react to state changes

## Slide 30: SEQ Operation #3
  state set according to second irmovl instruction
  combinational logic generates results for addl instruction

## Slide 31: SEQ Operation #4
  state set according to addl instruction
  combinational logic starting to react to state changes

## Slide 32: SEQ Operation #5
  state set according to addl instruction
  combinational logic generates results for je instruction

## Slide 33: SEQ Summary
Implementation
  Express every instruction as series of simple steps
  Follow same general flow for each instruction type
  Assemble registers, memories, predesigned combinational blocks
  Connect with control logic
Limitations
  Too slow to be practical
  In one cycle, must propagate through instruction memory, register file, ALU, and data memory
  Would need to run clock very slowly
  Hardware units only active for fraction of clock cycle